## Slide 1: EECS 489 Computer Networks Winter 2024
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Wireless network basics
802.11 Wireless LAN

## Slide 3: Recap: Point-to-point vs. broadcast medium
Point-to-point: dedicated pairwise communication
  E.g., long-distance fiber link
  E.g., Point-to-point link b/n Ethernet switch and host
Broadcast: shared wire or medium
  Traditional Ethernet (pre ~2000)
  802.11 wireless LAN

## Slide 4: Recap: Multiple access algorithm
Context: a shared broadcast channel
  Must avoid having multiple nodes speaking at once
    Otherwise, collisions lead to garbled data
  Need distributed algorithm to determine which node can transmit
Three classes of techniques
  Channel partitioning: divide channel into pieces
  Taking turns: scheme for deciding who transmits
  Random access: allow collisions, and then recover
    More in the Internet style!

## Slide 5: Recap: Random access MAC protocols
When node has packet to send
  Transmit at full channel data rate w/o coordination
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies
  How to detect and recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 6: Elements of a wireless network
network
infrastructure

## Slide 7: Elements of a wireless network
network
infrastructure
Wireless hosts
Laptop, smartphone
Run applications
May be stationary (non-mobile) or mobile
  Wireless does not always mean mobility

## Slide 8: Wireless vs. mobile
Wireless networks deal with communication over wireless links
Mobility deals with handling mobile users that change point of attachment to network
  Non-wireless networks may also have to deal with mobility issues
  Handoff: Mobile changes base station providing connection into wired network

## Slide 9: Elements of a wireless network
network
infrastructure
Base station
Typically connected to wired network
Relay: responsible for sending packets between wired network and wireless host(s) in its “area”
  E.g., cell towers, 802.11 access points (AP)

## Slide 10: Elements of a wireless network
network
infrastructure
Wireless link
Typically used to connect mobile(s) to base station
Also used as backbone link
Multiple access protocol coordinates link access
Various data rates, transmission distance

## Slide 11: Characteristics of selected wireless links
802.11 ax
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac

## Slide 12: Two modes of operation
Infrastructure mode: Base stations connect mobiles to wired network
Ad-hoc mode: Wireless hosts organize themselves to communicate

## Slide 13: Infrastructure mode
network
infrastructure

## Slide 14: Ad-hoc mode
No base station
Nodes can only transmit to other nodes within link coverage
Nodes organize themselves into a network: route among themselves

## Slide 15: Wireless network taxonomy
Single hop
Multiple hops
Infrastructure
(e.g., APs)
No
infrastructure
Host connects to
base station (WiFi,
WiMAX, cellular),
which connects to
larger Internet
No base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
Host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
No base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 16: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)

## Slide 17: Path loss/path attenuation
Free Space Path Loss (FSPL):
  d = distance
  λ = wave length (c/f)
  f = frequency
  c = speed of light
Due to
  Reflection, diffraction, absorption, terrain contours (urban, rural, vegetation), humidity
( )
FSPL =
4πdf
c
2
Notes: reduction in power density (attenuation) of an electromagnetic wave as it propagates through space.
Path loss may be due to many effects, such as free-space loss,refraction, diffraction, reflection, aperture-medium coupling loss, and absorption. Path loss is also influenced by terrain contours, environment (urban or rural, vegetation and foliage), propagation medium (dry or moist air), the distance between the transmitter and the receiver, and the height and location of antennas.

## Slide 18: SNR and BER
SNR: Signal-to-noise ratio
  Larger SNR makes it easier to extract signal from noise (good)
BER: Bit error rate
SNR vs. BER tradeoffs
  Given physical layer: Increase power → increase SNR → decrease BER
  Given SNR: Choose physical layer that meets BER requirement, giving highest throughput
  SNR may change with mobility: Dynamically adapt physical layer
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
Notes: BPSK: Binary phase-shift keying
QAM: Quadrature amplitude modulation

## Slide 19: Dealing with bit errors
Wired vs. wireless links: most loss due to congestion vs. higher, time-varying BER
Dealing with high wireless bit-error rates
  Sender could increase transmission power
    Needs hi energy (bad for battery-powered hosts)
    Creates more interference with other senders
  Stronger error detection and recovery
    More powerful error detection/correction codes
    Link-layer retransmission of corrupted frames
  Many TCP alternatives/extensions for wireless
    TCP Westwood uses Explicit Loss Notification (ELN)

## Slide 20: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving at destination at slightly different times

## Slide 21: Multipath effects
Signals bounce off surface and interfere with one another
Self-interference
S
R
Ceiling
Floor

## Slide 22: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving ad destination at slightly different times
  Interference from other sources: Standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
… make communication across (even a point-to-point) wireless link much more “difficult”

## Slide 23: Wireless network characteristics
Broadcast medium
  Anybody in proximity can hear and interfere
Cannot receive while transmitting
  Our own (or nearby) transmission is deafening our receiver ⇒ Half-duplex
  Recent work has shown that full duplex is possible
Signals sent by sender don’t always end up at receiver intact
Notes: Broadcast – anybody in proximity can hear and interfere (assuming the same channel)
Half-duplex: Not an engineering problem – but a fundamental physics that our strong transmission is deafening to our receiver.
Solve by different channels/bands for RX/TX

## Slide 24: Wireless network characteristics
Multiple wireless senders and receivers create many problems
  Multiple access issues (we’ve seen this before)
  Hidden terminal problem

## Slide 25: Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
Hence, A, C are unaware of their interference at B
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 26: 5-minute break!

## Slide 27: Announcements
Teaching evaluations
  75% or higher completion rate will result in +1 on the final grade for everyone

## Slide 28: 802.11 wireless LAN (aka WiFi)
Many variations
  802.11b, 802.11a, 802.11g, 802.11n, 802.11a*
All use CSMA/CA for multiple access
All have infrastructure and ad-hoc modes

## Slide 29: 802.11 LAN architecture
Wireless host communicates with base station
  Base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains
  Wireless hosts
  Access point (AP): base station
Ad-hoc mode: hosts only
BSS 1
BSS 2
Internet

## Slide 30: 802.11 LAN architecture
Designed for limited area
AP is set to specific channel
  Broadcast beacon messages with SSID (Service Set Identifier) and MAC Address periodically
Hosts scan all the channels to discover the AP’s
  Host associates with AP
BSS 1
BSS 2
Internet

## Slide 31: 802.11: Passive/active scanning
AP 2
AP 1
H1
BSS 2
BSS 1
1
2
3
1
Passive scanning
Beacon frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BSS 2
BSS 1
1
2
2
3
4
Active scanning
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent from H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 32: 802.11 multiple access
802.11 CSMA: sense before transmitting
  Don’t collide with ongoing transmissions by others
802.11 has no collision detection!
  Difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  Can’t sense all collisions in any case: hidden terminal, fading
Avoid collisions: CSMA/CA
  CA: Collision Avoidance

## Slide 33: Basic collision avoidance
Carrier sense:
  When medium busy, choose random interval
  Wait that many idle timeslots to pass before sending
When a collision is inferred, retransmit with binary exponential backoff (like Ethernet)
  Use ACK from receiver to infer “no collision”
  Use exponential backoff to adapt contention window
Notes: Why do we wait?
Why not just send right away as medium becomes clear?

## Slide 34: CSMA/CA
Before every data transmission
  Sender sends a Request to Send (RTS) frame with the length of transmission and the destination
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK
If sender doesn’t get a CTS back, it assumes collision
Sender
Receiver
Other node in
sender’s range
RTS
ACK
Data
CTS
Node outside
sender’s range
Notes: 34

## Slide 35: RTS/CTS
Works by reserving the channel using short frames before transferring much longer DATA frame
  Explicitly reserving the channel enables avoidance
Required to avoid hidden terminals
  Hidden terminals will hear CTS from the receiver

## Slide 36: Preventing collisions altogether
Frequency Spectrum partitioned into several channels
  Nodes within interference range can use separate channels
  Now A and C can send without any interference!
  Aggregate Network throughput doubles
A
B
C
D

## Slide 37: 802.11 frame: Addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 38: Why do we need Address 3?
Internet
router
H1
R1
H1 MAC addr AP MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
H1 MAC addr R1 MAC addr
dest. address
source address
802.3 frame

## Slide 39: Why do we need Address 3?
Internet
router
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame

## Slide 40: 802.11: Mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
Switch: which AP is associated with H1?
  Self-learning: Switch will see frame from H1 and “remember” which switch port can be used to reach H1
H1
BSS 2
BSS 1

## Slide 41: 802.15: Personal area network
802.15: evolved from Bluetooth specification
Less than 10 m diameter
Replacement for cables (mouse, keyboard, headphones)
Ad-hoc: no infrastructure
Master/slaves:
  Slaves request permission to send (to master)
  Master grants requests
M
radius of
coverage
S
S
S
P
P
P
P
M
S
Master device
P
Slave device
Parked device (inactive)

## Slide 42: Summary
Wireless networking introduces more challenges than wired networks
  Interference, attenuation, multipath, hidden terminals, etc.
CSMA/CD doesn’t work because collision detection is difficult
  Instead, CSMA/CA is used that avoid collisions by reserving the channel a priori