## Slide 1: EECS 489 Computer Networks Winter 2017
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Logistics
Exam at 220 CHRYS from 1:30PM to 3:30PM on Thursday, April 20
Open book/text/notes, but OFFLINE
Test does not require any complicated calculation
You’re NOT allowed to write/run any programs
No office hours for Nitish this week

## Slide 3: General guidelines (1)
Test only assumes material covered in lecture and sections
  Text: only to clarify details and context for the above
The test doesn’t require you to do complicated calculations
  Use this as a hint to determine if you’re on right track
You don’t need to memorize anything
You do need to understand how things work

## Slide 4: General guidelines (2)
Be prepared to:
  Weigh design options outside of the context we studied them in
  Contemplate new designs we haven’t covered in details but can be put together
    e.g., I introduce a new IP address format; how does this affect..”
  Reason from what you know about the pros/cons of solutions we did study

## Slide 5: General guidelines (3)
Exam format
  6 questions
  NO true/false or multiple choices
Questions not ordered in terms of complexity
    Read all carefully
Pace yourself accordingly!

## Slide 6: This review
Walk through what you’re expected to know since the midterm: key topics, important aspects of each
Not covered in review does NOT imply you don’t need to know it
  But if it’s covered today, you should know it
Summarize, not explain
  Stop me when you want to discuss something further!

## Slide 7: The networking stack
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Application
End system
Transport
Network
Datalink
Physical
Application
End system
Network
Datalink
Physical
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 8: Topics
Network layer (lectures 11–12, 14–18)
  Data plane
  Intra- and inter-domain routing
  SDN
Link layer (lectures 19–20, 23)
  Ethernet
  Wireless
Topics in networking (lectures 21–22)
  Datacenter
  Security

## Slide 9: Network layer
Present everywhere
Performs addressing, forwarding, and routing, among other tasks
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 10: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm
Very different timescales!

## Slide 11: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Control Plane
Data Plane

## Slide 12: Looking up the output port
One entry for each address  4 billion entries!
For scalability, addresses are aggregated
Notes: How does a router determine which output port for the packet!

## Slide 13: Longest prefix matching
110000**
110001**
1100****
1101****
ISP Router
Port 1
Port 2
Port 3
Port 4
Send to the port with the longest prefix match

## Slide 14: Routing: Local vs. global view
Local routing state is the forwarding table in a single router
  By itself, the state in a single router cannot be evaluated
  It must be evaluated in terms of the global context
Global state refers to the collection of forwarding tables in each of the routers
  Global state determines which paths packets take

## Slide 15: “Valid” routing state
Global state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
Goal of routing protocols: compute valid state
  How can we tell if routing state if valid?
Notes: What could go wrong?

## Slide 16: Necessary and sufficient condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing link (next-hop)
  A packet arrives, but the forwarding decision does not yield any outgoing link
A loop is when a packet cycles around the same set of nodes forever

## Slide 17: Least-cost routes
Least-cost routes provide an easy way to avoid loops
  No reasonable cost metric is minimized by traversing a loop
Least-cost paths form a spanning tree for each destination rooted at that destination

## Slide 18: Intra-domain routing
Link-state (LS) routing protocol
  Dijkstra’s algorithm
  Broadcast neighbors’ info to everyone
Distance vector (DV) routing protocol
  Bellman-Ford algorithm
  Gossip to neighbors about everyone

## Slide 19: Similarities between LS and DV routing
Both are shortest-path based routing
  Minimizing cost metric (link weights) a common optimization goal
    Routers share a common view as to what makes a path “good” and how to measure the “goodness” of a path
Due to shared goal, commonly used inside an organization
  RIP and OSPF are mostly used for intra-domain routing

## Slide 20: Comparison of LS and DV routing
Messaging complexity
LS: with N nodes, E links, O(NE) messages sent
DV: exchange between neighbors only
Speed of convergence
LS: relatively fast
DV: convergence time varies
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes its own table
DV:
  Node can advertise incorrect path cost
  Each node’s table used by others (error propagates)

## Slide 21: Addressing is key to scalable inter-domain routing
Ability to aggregate addresses is crucial for
  State: Small forwarding tables at routers
    Much less than the number of hosts
  Churn: Limited rate of change in routing tables

## Slide 22: Classful addressing
Three classes
  8-bit network prefix (Class A),
  16-bit network prefix (Class B), or
  24-bit network prefix (Class C)
Example: an organization needs 500 addresses.
  A single class C address is not enough (<500 hosts)
  Instead, a class B address is allocated (~65K hosts)
    Huge waste!

## Slide 23: CIDR: Classless inter-domain routing
Flexible division between network and host addresses
Offers a better tradeoff between size of the routing table and efficient use of the IP address space

## Slide 24: Administrative structure shapes Inter-domain routing
ASes want freedom to pick routes based on policy
ASes want autonomy
ASes want privacy

## Slide 25: Topology & policy shaped by inter-AS business relationship
Three basic kinds of relationships between ASes
  AS A can be AS B’s customer
  AS A can be AS B’s provider
  AS A can be AS B’s peer
Business implications
  Customer pays provider
  Peers don’t pay each other
    Exchange roughly equal traffic
Notes: Ehy???

## Slide 26: Business relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business implications

## Slide 27: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed

## Slide 28: BGP inspired by Distance-Vector with four differences
Shortest-path routes may not be picked to enforce policy
Path-Vector routing to avoid loops
Selective route advertisement may affect reachability
Routes may be aggregated for scalability

## Slide 29: Policy dictates how routes are “selected” and “exported”
Selection: Which path to use?
  Controls whether/how traffic leaves the network
Export: Which path to advertise?
  Controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 30: Typical export policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common – but not required! – practice)

## Slide 31: eBGP, iBGP, and IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  Distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intra-domain routing protocol
  Provide internal reachability
  E.g., OSPF, RIP

## Slide 32: eBGP, iBGP, and IGP together
Learn routes to external destination using eBGP
Distribute externally learned routes internally using iBGP
Travel shortest path to egress using IGP

## Slide 33: BGP attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 34: The field of networking
We have built a great artifact – the Internet
  It grew mostly unrelated to the academic research, which came later
CS networking today is largely the study of the Internet
BUT we do not really have an academic discipline

## Slide 35: “The Power of Abstraction”
“Modularity based on abstraction is the way things get done”
  Barbara Liskov
Abstractions  Interfaces  Modularity

## Slide 36: Analogy: Mainframe to PC evolution
Vertical integration, closed
Specialized application
Specialized operating system
Specialized hardware
Open interfaces
Arbitrary applications
Commodity operating systems
Microprocessor
We want the same for networking!

## Slide 37: Separate concerns with abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 38: Traditional fully decentralized control plane
Individual routing algorithm components in every router interact in the control plane
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane

## Slide 39: Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane
Remote Control

## Slide 40: SDN: Many challenges remain
Hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  Robustness to failures: leverage strong theory of reliable distributed system for control plane
  Security: “baked in” from day one?
Networks, protocols meeting mission-specific requirements
  E.g., real-time, ultra-reliable, ultra-secure
Internet-scaling

## Slide 41: 5-minute break!

## Slide 42: Topics
Network layer (lectures 11–12, 14–18)
  Data plane
  Intra- and inter-domain routing
  SDN
Link layer (lectures 19–20, 23)
  Ethernet
  Wireless
Topics in networking (lectures 21–22)
  Datacenter
  Security

## Slide 43: Data link layer
Provides four primary services
  Framing
    Encapsulates network layer data
  Link access
    Medium access control (MAC) protocol defines when to transmit frames
  Reliable delivery
    Primarily for mediums with high error rates (e.g., wireless)
  Error detection and correction

## Slide 44: Point-to-point vs. broadcast medium
Point-to-point: dedicated pairwise communication
  E.g., long-distance fiber link
  E.g., Point-to-point link b/n Ethernet switch and host
Broadcast: shared wire or medium
  Traditional Ethernet (pre ~2000)
  802.11 wireless LAN

## Slide 45: Random access MAC protocols
When node has packet to send
  Transmit at full channel data rate w/o coordination
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies
  How to detect and recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 46: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does not eliminate all collisions
  Why?

## Slide 47: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired (broadcast) LANs
  Compare transmitted, received signals
Collision detection difficult in wireless LANs
Notes: wireless: because reception while tx is difficult . broadcast isn’t perfect so collisions local

## Slide 48: Why switched Ethernet?
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions and no need for CSMA/CD
  No constraints on link lengths, etc.
Ethernet switch
A
B
C
D

## Slide 49: Ethernet switches are “self learning”
When a packet arrives:
  Inspect source MAC address, associate with incoming port
  Store mapping in the switch table
  Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 50: ARP and DHCP
Link layer discovery protocols
  ARP  Address Resolution Protocol
  DHCP  Dynamic Host Configuration Protocol
  Confined to a single local-area network (LAN)
  Rely on broadcast capability

## Slide 51: Key ideas in both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 52: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Consult the table when sending a packet
  Map dest. IP address to dest. MAC address
  Encapsulate (IP) data packet with MAC header; xmit
What if IP address not in the table?
  Sender broadcasts: Who has IP address 1.2.3.156?
  Receiver replies: MAC address 58-23-D7-FA-20-B0
  Sender caches result in its ARP table

## Slide 53: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 54: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving ad destination at slightly different times
  Interference from other sources: Standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
… make communication across (even a point-to-point) wireless link much more “difficult”

## Slide 55: Wireless network characteristics
Multiple wireless senders and receivers create many problems
  Multiple access issues (we’ve seen this before)
  Hidden terminal problem

## Slide 56: Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
Hence, A, C are unaware of their interference at B
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 57: CSMA/CA
Before every data transmission
  Sender sends a Request to Send (RTS) frame with the length of transmission and the destination
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK
If sender doesn’t get a CTS back, it assumes collision
Sender
Receiver
Other node in
sender’s range
RTS
ACK
Data
CTS
Notes: 57

## Slide 58: Topics
Network layer (lectures 11–12, 14–18)
  Data plane
  Intra- and inter-domain routing
  SDN
Link layer (lectures 19–20, 23)
  Ethernet
  Wireless
Topics in networking (lectures 21–22)
  Datacenter
  Security

## Slide 59: Datacenter applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 60: Datacenter traffic characteristics
Two key characteristics
  Most flows are small
  Most bytes come from large flows
Applications want
  High bandwidth (large flows)
  Low latency (small flows)

## Slide 61: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 62: Datacenter networking stack
Networking in modern datacenters
  L2/L3 design
    Addressing / routing / forwarding in the Fat-Tree
  L4 design
    Transport protocol design (w/ Fat-Tree)
  L7 design
    Exploiting application-level information (w/ Fat-Tree)

## Slide 63: Using multiple paths well

## Slide 64: L2/L3 highlights
Load balancing while forwarding
  Per-packet
  Per-flow
Hard-coded addressing or via indirection
Modified LS/DV or source routing

## Slide 65: L4 highlights
Tension between high throughput and low latency requirements
  Deep queues vs shallow queues
DCTCP
  React early, quickly, and with certainty using ECN
  React in proportion to the extent of congestion, not its presence

## Slide 66: L7 highlights
What do applications care about?
  Flow completion time (FCT)
  Coflow completion time (CCT)
    A coflow is a collection of flows with a shared application-level objective
Coflow-based networking
  Managed
  Centralized

## Slide 67: General goals for communication security: CIA
Confidentiality
  No one read our communication
  Cryptography
Message Integrity
  No one can modify our communication w/o detection
  Verification
Availability and Authentication
  Only we can access our data and communicate on our behalf
  Redundancy, DoS/DDoS prevention

## Slide 68: Summary
You are undoubtedly the best undergraduate class I’ve taught ;)
  THANK YOU SO MUCH!!!
Do great things!