## Slide 1: EECS 489 Computer Networks Winter 2024
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Video streaming
Datacenter applications

## Slide 3: Recap: TTL in dig output is in seconds
dig nyu.edu
; <<>> DiG 9.10.6 <<>> nyu.edu
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 64269
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 512
;; QUESTION SECTION:
;nyu.edu. IN A
;; ANSWER SECTION:
nyu.edu. 60 IN A 216.165.61.24
;; Query time: 79 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Fri Jan 19 11:07:26 EST 2024
;; MSG SIZE rcvd: 52
TTL
Notes: 60 Seconds

## Slide 4: Why is video important?
Dominates the global Internet traffic landscape
  About 65%, i.e., every 2 of 3 bytes in 2023!
Major sources
  Netflix
  YouTube
  …

## Slide 5: How to watch a video?
Download and watch
  Often too large to send in one GET
  Doesn’t even make sense even if its possible
    Users have to wait too long
    Users may skip forward! ⇒ bandwidth waste
    User’s connection quality may change (e.g., switching from WiFi to LTE) ⇒ lower resolution to match bandwidth
Our focus is not live video

## Slide 6: The video medium
Video is a sequence of images/frames displayed at a constant rate (moving pictures)
Digital image is an array of pixels, each pixel represented by bits
Examples:
  Single frame image encoding: 1024x1024 pixels, 24 bits/pixel ⇒ 3 MB/image
  Movies: 24 frames/sec ⇒ 72 MB/sec
  TV: 30 frames/sec ⇒ 90 MB/sec

## Slide 7: The video medium (cont’d)
Compression is key
  Lots of algorithms to compress
The same video can be (and typically is) compressed to multiple quality levels
  E.g., 480p, 720p, 1080p, 4K
Why multiple resolutions?
  Adapt to conditions

## Slide 8: How do we serve video?
It’s in the name!
  Video streaming

## Slide 9: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while. Why?
  To minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 10: HTTP streaming
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network delay
(fixed in this example)
time
3. video received,
played out at client
(30 frames/sec)

## Slide 11: Challenges
Absorb network delay variations
Handle user interactions
  Jump forward, fast-forward, rewind, pause
Handle packet loss, retransmission etc.

## Slide 12: HTTP streaming: Revisited
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
Client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 13: Issues with HTTP streaming
Same bitrate for all clients
  Clients can have very different network conditions
  Clients network conditions can change over time
Cannot dynamically adapt to conditions

## Slide 14: DASH : Dynamic Adaptive Streaming over HTTP
Keep multiple resolutions of the same video
  Stored in a manifest file in the HTTP server
Client asks for the manifest file first to learn about the options
Asks for chunks at a time and measures available bandwidth while they are downloaded
  Low bandwidth ⇒ switch to lower bitrate
  High bandwidth ⇒ switch to higher bitrate
Adaptive bit rate (ABR)

## Slide 15: Cloud Systems

## Slide 16: Who’s serving Web services?
User
Server
HTTP GET

## Slide 17: Who’s serving Web services?
User
Server
HTTP Response
<html>
<body>
... …
</body>
</html>

## Slide 18: Cloud datacenters run the world
Source: Google

## Slide 19: Cloud datacenters run the world
Source: Google

## Slide 20: Cloud datacenters run the world
Source: Facebook

## Slide 21: How big is a datacenter (DC)?
1M servers/site [Microsoft/Amazon/Google]
> $1B to build one site [Facebook]
>$20M/month/site operational costs [MS’09]
Data center hardware spending grew to $185 billion in 2021. [Synergy Research Group report]
But only O(100) sites

## Slide 22: Implications (1)
Scale
  Need scalable designs
  Low-cost designs: e.g., use commodity technology
  High utilization (efficiency): e.g., >60% avg. utilization
    Contrast: avg. utilization on Internet links often ~30%
  Tolerate frequent failure
    Large number of (low cost) components
  Automate

## Slide 23: Implications (2)
Service model: clouds / multi-tenancy
  Performance guarantees
  Isolation guarantees
  Portability

## Slide 24: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 25: Partition-Aggregate
eecs 489
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 26: Partition-Aggregate
eecs 489
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 27: End-to-end response time
Less than 200 milliseconds between receiving user query in the browser and displaying the results
  RTT = O(10) to 100 milliseconds
  What remains?
Next time, when the page is not loading fast enough, think about the poor servers working for you 

## Slide 28: 5-minute break!

## Slide 29: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 30: Map-Reduce
Reduce Stage
Map Stage
The most popular software that follows this paradigm is Apache Spark

## Slide 31: Datacenter networks
Server
ToR Switch
Aggregation

## Slide 32: Datacenter networks (Cont.)
Rack
Aggregation
Core

## Slide 33: Datacenter traffic
Rack
Aggregation
Core
North-South Traffic
East-West Traffic

## Slide 34: East-West traffic
Traffic between servers in the datacenter
Communication within “big data” computations
Traffic may shift on small timescales (< minutes)

## Slide 35: Datacenter traffic characteristics
Two key characteristics
  Most flows are small
  Most bytes come from large flows
Applications want
  High bandwidth (large flows)
  Low latency (small flows)

## Slide 36: High bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: Datacenter network as one giant switch

## Slide 37: Datacenter network as one giant switch

## Slide 38: Datacenter network as one giant switch

## Slide 39: Datacenter network as one giant switch
One
GIANT
Switch

## Slide 40: High bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: Datacenter network as one giant switch
  Would require a 10 Pbits/sec switch!
    1M ports (one port/server)
    10Gbps per port
Practical approach: build a network of switches (“fabric”) with high “bisection bandwidth”
  Each switch has practical #ports and link speeds

## Slide 41: Bisection bandwidth
Partition a network into two equal parts
Minimum bandwidth between the partitions is the bisection bandwidth
Full bisection bandwidth: bisection bandwidth in an N node network is N/2 times the bandwidth of a single link
  Nodes of any two halves can communicate at full speed with each other

## Slide 42: Achieving full bisection bandwidth
Scale up
  Make links fatter toward the core of the network
Problem: Scaling up a traditional tree topology is expensive!
  Requires non-commodity / impractical / link and switch components
Solutions?
  Over-subscribe (i.e., provision less than full BBW)
  Better topologies

## Slide 43: Oversubscription
Need techniques to avoid congesting oversubscribed links!
10G
20G
40G
10G
10G
20G

## Slide 44: Oversubscription
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 45: Better topologies
Rack
Aggregation
Core

## Slide 46: Better topologies
Rack
Aggregation
Core

## Slide 47: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 48: Challenges in scale-out designs?
Topology offers high bisection bandwidth
All other system components must be able to exploit this available capacity
  Routing must use all paths
  Transport protocol must fill all pipes (fast)

## Slide 49: Summary
Video streaming
  Too large to send, so stream it
  Dynamically adapt to the network and users
Cloud systems
  Forms the backend of modern web services
  Runs in datacenters where all the processing happens