## Slide 1: EECS 489 Computer Networks Winter 2024
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Xin Jin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Software-defined networking
Programmable networks

## Slide 3: The field of networking
CS networking today is largely the study of the Internet
  Perhaps the only history class many will take in CS

## Slide 4: Building an artifact, not a discipline
Other fields in “systems”: OS, DB, etc.
  Teach basic principles
  Are easily managed
  Continue to evolve
Networking:
  Teach big bag of protocols
  Notoriously difficult to manage
  Evolves very slowly
Networks are much more primitive and less understood than other computer systems

## Slide 5: A tale of two planes
Data plane: forwarding packets
  Based on local forwarding state
Control plane: computing that forwarding state
  Involves coordination with rest of system

## Slide 6: Original goals for the control plane
Basic connectivity: route packets to destination
  Local state computed by routing protocols
  Globally distributed algorithms
Inter-domain policy: find policy-compliant paths
  Done by globally distributed BGP
What other goals are there in running a network?

## Slide 7: Extended roles of the control plane
Performs various network management tasks
  For example,
    Where to route?
    How much to route?
    At what rate to route?
    Should we route at all?
    …

## Slide 8: Bottom line
Many different control plane mechanisms
Each designed from scratch for their intended goal
Encompassing a wide variety of implementations
  Distributed, manual, centralized,…
None of them particularly well designed
Network control plane is a complicated mess!

## Slide 9: “The Power of Abstraction”
“Modularity based on abstraction is the way things get done”
  Barbara Liskov
Abstractions  Interfaces  Modularity

## Slide 10: Analogy: Mainframe to PC evolution
Vertical integration, closed
Specialized application
Specialized operating system
Specialized hardware
Open interfaces
Arbitrary applications
Commodity operating systems
Microprocessor
We want the same for networking!

## Slide 11: Many control plane mechanisms
Variety of goals, no modularity
  Routing: distributed routing algorithms
  Isolation: ACLs, Firewalls,…
  Traffic engineering: adjusting weights,…
Control Plane: mechanism without abstraction
  Too many mechanisms, not enough functionality

## Slide 12: Task: Compute forwarding state
Consistent with low-level hardware/software
  Which might depend on vendor
Based on entire network topology
  Because many control decisions depend on topology
For all routers/switches in network
  Every router/switch needs forwarding state

## Slide 13: Separate concerns with abstractions
Be compatible with low-level hardware/software
  Forwarding abstraction
Make decisions based on entire network
  Network state abstraction
Compute configuration of each physical device
  Specification abstraction

## Slide 14: #1: Forwarding abstraction
Express intent independent of implementation
  Don’t want to deal with proprietary HW and SW
Design details concern exact nature of:
  Header matching
  Allowed actions

## Slide 15: #2: Network state abstraction
Abstraction: global network view
  Annotated network graph provided through an API
Creates a logically centralized view of the network (Network Operating System)
  Runs on replicated servers in network (“controllers”)
Information flows both ways
  Information from routers/switches to form “view”
  Configurations to routers/switches to control forwarding

## Slide 16: #3: Specification abstraction
Control mechanism expresses desired behavior
  Whether it be isolation, access control, or QoS
It should not be responsible for implementing that behavior on physical network infrastructure
  Requires configuring the forwarding tables in each switch
Abstract view of network
  Models only enough detail to specify goals
  Will depend on task semantics

## Slide 17: Traditional fully decentralized control plane
Individual routing algorithm components in every router interact in the control plane
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane

## Slide 18: Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane
Remote Control

## Slide 19: Each goal is an app via specification abstraction
What if an operator wants X?
What if a customer wants to do weighted traffic splitting?
…
There is an app for it!
  Write your own routing protocol, load balancing algorithm, access control policies

## Slide 20: Reason about each app via network state abstraction
Now that the network is not distributed anymore and is a simple graph, we can verify whatever the correctness of whatever we specified

## Slide 21: Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Each router contains a flow table
Each entry of the flow table defines a match-action rule
Entries of the flow table is computed and distributed by the (logically) centralized controller

## Slide 22: SDN: Many challenges remain
Hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  Robustness to failures: leverage strong theory of reliable distributed system for control plane
  Dependability, security: “baked in” from day one?
Networks, protocols meeting mission-specific requirements
  E.g., real-time, ultra-reliable, ultra-secure
Internet-scaling

## Slide 23: Some progress in the wide-area network (WAN)
Google and Microsoft use SDN to manage traffic between datacenters
One centralized controller to rule the entire world (well, their world)

## Slide 24: 5-minute break!

## Slide 25: A tale of two planes
Data plane: forwarding packets
  Based on local forwarding state
Control plane: computing that forwarding state
  Involves coordination with rest of system

## Slide 26: OpenFlow data plane abstraction
Flow is defined by header fields
Generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 27: OpenFlow: Flow table entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: Now I’ll describe the API that tries to meet these goals.
27

## Slide 28: Forwarding abstraction
Router
  Match: longest destination IP prefix
  Action: forward out a link
Switch
  Match: destination MAC address
  Action: forward or flood
Firewall
  Match: IP addresses and TCP/UDP port numbers
  Action: permit or deny
NAT
  Match: IP address and port
  Action: rewrite address and port
Match + Action: unifies different kinds of devices

## Slide 29: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 30: OpenFlow protocol
Operates between controller, switch
TCP used to exchange messages
  Optional encryption
Three classes of OpenFlow messages:
  Controller-to-switch
  Asynchronous (switch to controller)
  Symmetric (misc.)
OpenFlow Controller

## Slide 31: Fixed-function data plane
Traditional switches are fixed-function
  They can do whatever they can do at birth, but they cannot change!
  Bottom-up design
Even OpenFlow was designed to be a fixed protocol
  With a fixed table format
  Capable of doing limited things

## Slide 32: Takes forever to get a feature
Network Equipment Vendor
Network Owner
ASIC
Team
Software
Team
Feature
Weeks
Years
Years
Feature
Feature

## Slide 33: Programmable data plane
What if we could tell switches exactly what we want?
  What table to keep?
  What rules to use?
  What data to keep track of?
  …

## Slide 34: Top-down approach
Precisely specify what you want to do and how you want a packet to be processed
table int_table {
reads {
ip.protocol
}
actions {
export_queue_latency
}
}
action export_queue_latency (sw_id) {
add_header(int_header);
modify_field(int_header.kind, TCP_OPTION_INT);
modify_field(int_header.len, TCP_OPTION_INT_LEN);
modify_field(int_header.sw_id, sw_id);
modify_field(int_header.q_latency,
intrinsic_metadata.deq_timedelta);
add_to_field(tcp.dataOffset, 2);
add_to_field(ipv4.totalLen, 8);
subtract_from_field(ingress_metadata.tcpLength, 12);
}

## Slide 35: What’s left?
Compile it down to be something runnable on a programmable switch
  Similar to other high-level languages we use to run code on hardware like CPU, GPU, FPGA etc.
  P4 for programmable switches
But which switch?

## Slide 36: PISA: Protocol Independent Switch Architecture
Match + Action
Memory
ALU
Programmable
Parser
Programmer declares which
headers are recognized
Programmer declares what
tables are needed and how packets are processed
All stages are identical – makes PISA a good “compiler target”

## Slide 37: How’s programmability used today?
Remove features to reduce complexity
Add proprietary features
Silicon independence or avoid vendor lock-in
Telemetry and measurements

## Slide 38: Example: In-band network telemetry (INT)
“Which path did my packet take?”
“Which rules did my packet follow?”
“How long did it queue at each switch?”
“Who did it share the queues with?”

## Slide 39: Why now?
One of the earlier incarnation of programmable networks was in mid 90s
  Active networks
What’s changed after two+ decades?
  Hardware: We can now make programmable switches as fast as fixed ones
  Software: We have found a (so far) reasonable balance between programmability, performance, and security

## Slide 40: Summary
Abstractions beget modularity
  Modularity is (almost always) good
Programmability is powerful
  Finding the right balance is hard
Next lecture: Layer 2

## Slide 42: Traffic engineering
Want to avoid persistent overloads on links
Choose routes to spread traffic load across links

## Slide 43: Traffic engineering: Difficult
Q: What if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: Need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Link weights are only control “knobs”
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 44: Traffic engineering: Difficult
Q: What if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: Can’t do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 45: Traffic engineering: Difficult
Q: What if w wants to route the two flows differently?
A: Can’t do it (with LS or DV)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 46: OpenFlow: Controller-to-switch messages
Key controller-to-switch messages
  Features: controller queries switch features, switch replies
  Configure: controller queries/sets switch configuration parameters
  Modify-state: add, delete, modify flow entries in the OpenFlow tables
  Packet-out: controller can send this packet out of specific switch port

## Slide 47: OpenFlow: Switch-to-controller messages
Key switch-to-controller messages
  Packet-in: transfer packet (and its control) to controller. See packet-out message from controller
  Flow-removed: flow table entry deleted at switch
  Port status: inform controller of a change on a port
Network operators do not “program” switches by creating/sending OpenFlow messages directly.
  Instead, they use higher-level abstraction at controller