## Slide 1: EECS 489 Computer Networks Winter 2017
Mosharaf Chowdhury

## Slide 2: Agenda
Overview of the basics
  How is the network shared?
  How do we evaluate a network?
  What is a network made of?

## Slide 3: Switched networks
End-systems and networks connected by switches instead of directly connecting them
Allows us to scale
  For example, directly connecting N nodes to each other would require N2 links!

## Slide 4: When do we need to share the network?
Switch and link resources

## Slide 5: Two ways to share switched networks
Circuit switching
  Resource reserved per connection
  Admission control: per connection
Packet switching via statistical multiplexing
  Packets treated independently, on-demand
  Admission control: per packet
Hybrid: virtual circuits
  Emulating circuit switching with packets (see text)

## Slide 6: Circuit switching
src sends reservation request to dst
Switches create circuit after admission control
src sends data
src sends teardown request
dst
src
10 Mbps?
10 Mbps?
✔️
✔️

## Slide 7: Circuit switching
Reservation establishes a “circuit” within a switch
switch
src
dst

## Slide 8: Many kinds of circuits
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 9: Timing in circuit switching
time

## Slide 10: Timing in circuit switching
time

## Slide 11: Timing in circuit switching
time

## Slide 12: Timing in circuit switching
time

## Slide 13: Timing in circuit switching
time
Circuit establishment

## Slide 14: Timing in circuit switching
Data
time
Circuit establishment
Data transfer

## Slide 15: Timing in circuit switching
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 16: Why the delays?
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 17: Timing in circuit switching
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 18: Timing in circuit switching
Data
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 19: Timing in circuit switching
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 20: Circuit switching
Pros
  Predictable performance
  Simple/fast switching (once circuit established)
Cons
  Complexity of circuit setup/teardown
  Inefficient when traffic is bursty
  Circuit setup adds delay
  Switch fails  its circuit(s) fails

## Slide 21: Packet switching
Each packet contains destination (dst)
Each packet treated independently
switch
dst

## Slide 22: Packet switching
Each packet contains destination (dst)
Each packet treated independently
With buffers to absolve transient overloads
switch
dst

## Slide 23: Packet switching
Pros
  Efficient use of network resources
  Simpler to implement
  Robust: can “route around trouble”
Cons
  Unpredictable performance
  Requires buffer management and congestion control

## Slide 24: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Results in unpredictability
  Works well except for the extreme cases

## Slide 25: 5-minute break!

## Slide 26: Announcements
Discussion sections start this week
  Check course webpage for times, dates, locations
Assignment 1 is live!
  Sign up your individual GitHub id at https://goo.gl/forms/ivNarhVVC63hSG703
Wait-listed students will be enrolled as and when registered students drop the class
  If you’re planning to drop, please do so soon!

## Slide 27: How do we evaluate a network?

## Slide 28: Performance metrics
Delay
Loss
Throughput

## Slide 29: Delay
How long does it take to send a packet from its source to destination?

## Slide 30: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 31: A network link
Link bandwidth
  Number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time
BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 32: Examples
Same city over a slow link:
  Bandwidth: ~100Mbps
  Propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Cross-country over fast link:
  Bandwidth: ~10Gbps
  Propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)

## Slide 33: 1. Transmission delay
How long does it take to push all the bits of a packet into a link?
Packet size / Transmission rate of the link
  e.g., 1000 bits / 100 Mbits per sec = 10-5 sec

## Slide 34: 2. Propagation delay
How long does it take to move one bit from one end of a link to the other?
Link length / Propagation speed of link
  E.g., 30 kilometers / 3*108 meters per sec = 10-4 sec

## Slide 35: Packet delay Sending a 100-byte packet
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 36: Packet delay Sending a 100-byte packet
time=0
A
B
100Byte packet
Time
1Gbps, 1ms
Time to transmit one bit = 1/109s
Time to transmit 800 bits=800x1/109s
Time when that bit reaches B = 1/109+1/103s
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms

## Slide 37: Sending a large file using 100-byte packets
100Byte packet
100Byte packet
A
B
100Byte packet
1Gbps, 1ms

## Slide 38: Pipe view of a link
Transmission delay decreases as bandwidth increases
time
bandwidth
transmission delay

## Slide 39: 3. Queuing delay
How long does a packet have to sit in a buffer before it is processed?

## Slide 40: Queueing delay: “pipe” view

## Slide 41: Queueing delay: “pipe” view
No overload!

## Slide 42: Queueing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 43: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 44: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 45: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 46: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 47: Persistent overload leads to packet loss
Queue

## Slide 48: Queueing delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
  Arrival rate at the queue
  Nature of arriving traffic (bursty or not?)
  Transmission rate of outgoing link

## Slide 49: Queueing delay
How long does a packet have to sit in a buffer before it is processed?
Characterized with statistical measures
  Average queuing delay
  Variance of queuing delay
  Probability delay exceeds a threshold value

## Slide 50: Basic queueing theory terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 51: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  How often does a single packet get counted? W times
Why do you care?
  Easy to compute L, harder to compute W
Notes: Row vs column

## Slide 52: 4. Processing Delay
How long does the switch take to process a packet?
  Negligible

## Slide 53: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation

## Slide 54: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 55: Throughput
At what rate is the destination receiving data from the source

## Slide 56: Throughput
F/R + propagation delay
Transmission rate R bits/sec
Average throughput =
Transfer time (T) =
File of size F bits
F/T ≈ R
Packets of size L bits

## Slide 57: End-to-end throughput
Transmission rate R
File of size F bits
Packets of size L bits
Transmission rate R’ > R
Average throughput =
min{R, R’} = R
bottleneck link

## Slide 58: Summary
How is it shared?
  On-demand or via reservation
How do we evaluate a network?
  Bandwidth, delay, loss, BDP, …
What is a network made of?
  Whatever physical infrastructure exist
  See backup slides

## Slide 60: What is the network made of?

## Slide 61: What is a network made of?
link
switch
end-system
Internet Service Provider

## Slide 62: What is a network made of?
phone company

## Slide 63: What is a network made of?
phone company

## Slide 64: The last hop
home PC
switch

## Slide 65: How do we connect?
home PC
switch
DSL modem
DSLAM
central office
phone line
telephone
telephone network
...
Notes: DSLAM: Digital Subscriber Line Access Multiplexer

## Slide 66: Digital Subscriber Line (DSL)
Twisted pair copper
3 separate channels
  downstream data channel
  upstream data channel
  2-way phone channel
up to 25 Mbps downstream
up to 2.5 Mbps upstream

## Slide 67: How about an cable provider as an ISP?
cable company

## Slide 68: Connecting via cable
home PC
switch
cable modem
CMTS
cable head end
copper
fiber
...
Notes: CMTS: Cable Modem Termination System

## Slide 69: Cable
Coaxial copper & fiber
Up to 42.8 Mbps downstream
Up to 30.7 Mbps upstream
Shared broadcast medium

## Slide 70: Any other means?
university net

## Slide 71: Ethernet
workstation
“aggregate” switch
Ethernet cable
“local” switch
...

## Slide 72: Ethernet
Twisted pair copper
100 Mbps, 1 Gbps, 10 Gbps (each direction)

## Slide 73: Many other ways
Cellular (smart phones)
Satellite (remote areas)
Fiber to the Home (home)
Optical carrier (Internet backbone)

## Slide 74: Where is WiFi?
WiFi
WiFi
WiFi