## Slide 1: EECS 489 Computer Networks Fall 2018
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
TCP congestion control wrap-up
TCP throughput equation
Problems with congestion control

## Slide 3: Recap
Flow Control
  Restrict window to RWND to make sure that the receiver isn’t overwhelmed
Congestion Control
  Restrict window to CWND to make sure that the network isn’t overwhelmed
Together
  Restrict window to min{RWND, CWND} to make sure that neither the receiver nor the network are overwhelmed

## Slide 4: CC Implementation
States at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
  dupACKcount and timer
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 5: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence, after one RTT with no drops: CWND = 2xCWND

## Slide 6: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence, after one RTT with no drops: CWND = CWND + 1
Congestion avoidance phase

## Slide 7: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 8: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 9: Example
t
Window
Slow-start restart: Go back to CWND = 1 MSS, but take advantage of knowing the previous value of CWND
Slow start in operation until it reaches half of previous CWND, i.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 10: Not done yet!
Problem: congestion avoidance too slow in recovering from an isolated loss

## Slide 11: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped

## Slide 12: Timeline: [101, 102, …, 110]
ACK 101 (due to 102) cwnd=10 dupACK#1 (no xmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (no xmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (no xmit)
RETRANSMIT 101 ssthresh=5 cwnd= 5
ACK 101 (due to 105) cwnd=5 + 1/5 (no xmit)
ACK 101 (due to 106) cwnd=5 + 2/5 (no xmit)
ACK 101 (due to 107) cwnd=5 + 3/5 (no xmit)
ACK 101 (due to 108) cwnd=5 + 4/5 (no xmit)
ACK 101 (due to 109) cwnd=5 + 5/5 (no xmit)
ACK 101 (due to 110) cwnd=6 + 1/6 (no xmit)
ACK 111 (due to 101)  only now can we transmit new packets
Plus no packets in flight so ACK “clocking” (to increase CWND) stalls for another RTT
✗

## Slide 13: Solution: Fast recovery
Idea: Grant the sender temporary “credit” for each dupACK so as to keep packets in flight
If dupACKcount = 3
  ssthresh = CWND/2
  CWND = ssthresh + 3
While in fast recovery
  CWND = CWND + 1 for each additional dupACK
Exit fast recovery after receiving new ACK
  set CWND = ssthresh

## Slide 14: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped

## Slide 15: Timeline: [101, 102, …, 110]
ACK 101 (due to 102) cwnd=10 dup#1
ACK 101 (due to 103) cwnd=10 dup#2
ACK 101 (due to 104) cwnd=10 dup#3
RETRANSMIT 101 ssthresh=5 cwnd= 8 (5+3)
ACK 101 (due to 105) cwnd= 9 (no xmit)
ACK 101 (due to 106) cwnd=10 (no xmit)
ACK 101 (due to 107) cwnd=11 (xmit 111)
ACK 101 (due to 108) cwnd=12 (xmit 112)
ACK 101 (due to 109) cwnd=13 (xmit 113)
ACK 101 (due to 110) cwnd=14 (xmit 114)
ACK 111 (due to 101) cwnd = 5 (xmit 115)  exiting fast recovery
Packets 111-114 already in flight
ACK 112 (due to 111) cwnd = 5 + 1/5  back in cong. avoidance
✗

## Slide 16: TCP state machine
Slow Start
Cong. Avoid.
Fast Recovery
CWND > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 17: Timeouts ➔ Slow Start
Slow Start
Cong. Avoid.
Fast Recovery
CWND > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 18: dupACKs ➔ Fast Recovery
Slow Start
Cong. Avoid.
Fast Recovery
CWND > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 19: New ACK changes state ONLY from Fast Recovery
Slow Start
Cong. Avoid.
Fast Recovery
CWND > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 20: TCP state machine
Slow Start
Cong. Avoid.
Fast Recovery
CWND > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 21: TCP flavors
TCP-Tahoe
  CWND =1 on 3 dupACKs
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on 3 dupACKs
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  Incorporates selective acknowledgements
Our default assumption

## Slide 22: How can they coexist?
All follow the same principle
  Increase CWND on good news
  Decrease CWND on bad news

## Slide 23: 5-minute break!

## Slide 24: Announcements
Next lecture on October 17

## Slide 25: TCP Throughput Equation

## Slide 26: A simple model for TCP throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 27: A simple model for TCP throughput
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 28: Implications (1): Different RTTs
Flows get throughput inversely proportional to RTT
TCP unfair in the face of heterogeneous RTTs!
A1
A2
B2
B1
bottleneck
link
100ms
200ms

## Slide 29: Implications (2): High-speed TCP
Assume RTT = 100ms, MSS=1500bytes, BW=100Gbps
What value of p is required to reach 100Gbps throughput?
  ~ 2 x 10-12
How long between drops?
  ~ 16.6 hours
How much data has been sent in this time?
  ~ 6 petabits

## Slide 30: Adapting TCP to high speed
Once past a threshold speed, increase CWND faster
  A proposed standard [Floyd’03]: once speed is past some threshold, change equation to p-.8 rather than p-.5
  Let the additive constant in AIMD depend on CWND
Other approaches?
  Multiple simultaneous connections (hack but works today)
  Router-assisted approaches

## Slide 31: Implications (3): Rate-based CC
TCP throughput is swings between W/2 to W
Apps may prefer steady rates (e.g., streaming)
“Equation-Based Congestion Control”
  Ignore TCP’s increase/decrease rules and just follow the equation
  Measure drop percentage p, and set rate accordingly
Following the TCP equation ensures “TCP friendliness”
  i.e., use no more than TCP does in similar setting

## Slide 32: Implications (4): Loss not due to congestion?
TCP will confuse corruption with congestion
Flow will cut its rate
  Throughput ~ 1/sqrt(p) where p is loss prob.
  Applies even for non-congestion losses!

## Slide 33: Implications (5): Short flows cannot ramp up
50% of flows have < 1500B to send; 80% < 100KB
Implications
  Short flows never leave slow start!
    They never attain their fair share
  Too few packets to trigger dupACKs
    Isolated loss may lead to timeouts
    At typical timeout values of ~500ms, might severely impact flow completion time

## Slide 34: Implications (6): Short flows share long delays
A flow deliberately overshoots capacity, until it experiences a drop
Means that delays are large, and are large for everyone
  Consider a flow transferring a 10GB file sharing a bottleneck link with 10 flows transferring 100B
  Larger flows dominate smaller ones

## Slide 35: Implications (7): Cheating
Three easy ways to cheat
  Increasing CWND faster than +1 MSS per RTT

## Slide 36: Implications (7): Cheating
Three easy ways to cheat
  Increasing CWND faster than +1 MSS per RTT
  Using large initial CWND
    Common practice by many companies

## Slide 37: Implications (7): Cheating
Three easy ways to cheat
  Increasing CWND faster than +1 MSS per RTT
  Using large initial CWND
    Common practice by many companies
  Opening many connections

## Slide 38: Open many connections
Assume
  A starts 10 connections to B
  D starts 1 connection to E
  Each connection gets about the same throughput
Then A gets 10 times more throughput than D
A
B
x
D
E
y

## Slide 39: Implications (8): CC intertwined with reliability
CWND adjusted based on ACKs and timeouts
Cumulative ACKs and fast retransmit/recovery rules
Complicates evolution
  Changing from cumulative to selective ACKs is hard
Sometimes we want CC but not reliability
  e.g., real-time applications
We may also want reliability without CC

## Slide 40: Recap: TCP problems
Misled by non-congestion losses
Fills up queues leading to high delays
Short flows complete before discovering available capacity
AIMD impractical for high speed links
Saw tooth discovery too choppy for some apps
Unfair under heterogeneous RTTs
Tight coupling with reliability mechanisms
End hosts can cheat
Routers tell endpoints if they’re congested
Routers tell endpoints what rate to send at
Routers enforce fair sharing
Could fix many of these with some help from routers!

## Slide 41: Summary
TCP works even though it has many flaws
Many of them can be fixed via assistance from the network
Next few weeks: The Network Layer