## Slide 1: EECS 489 Computer Networks Fall 2020
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
How is communication organized?

## Slide 3: What we want
http://123.xyz
123.xyz server

## Slide 4: (Some of) What happens…
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 5: (More of) What happens
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 6: What we get
http://123.xyz
123.xyz server

## Slide 7: Inspiration…
Dear John,
Your days are numbered.
--Pat
CEO A writes letter to CEO B

## Slide 8: Inspiration…
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company

## Slide 9: The path of the letter
CEO
Aide
FedEx
CEO
Aide
FedEx
FedEx Envelope (FE)
Letter
Envelope

## Slide 10: The path of the letter
CEO
Aide
FedEx
CEO
Aide
FedEx
“Peers” in same layer understand each other
No one else needs to
Lowest level has most packaging
Letter
Envelope
Semantic Content
Identity
FedEx Envelope (FE)
Location

## Slide 11: Three steps
Decompose the problem into tasks
Organize these tasks
Assign tasks to entities (who does what)

## Slide 12: Back to the Internet: Decomposition
Applications
Physical transfer of bits
Best-effort local packet delivery
Best-effort global packet delivery
Reliable or unreliable transport
in built on
in built on
in built on
in built on

## Slide 13: Communication organization
Application
Applications
Physical transfer of bits
Best-effort local packet delivery
Best-effort global packet delivery
Reliable or unreliable transport
in built on
in built on
in built on
in built on
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1

## Slide 14: OSI layers
OSI stands for Open Systems Interconnection model
  Developed by the ISO
Session and presentation layers are often implemented as part of the application layer
Application
Presentation
Session
L7
L6
L5
Transport
Network
Data link
Physical
L4
L3
L2
L1

## Slide 15: Layers
Layer: a part of a system with well-defined interfaces to other parts
One layer interacts only with layer above and layer below
Two layers interact only through the interface between them

## Slide 16: Layers and protocols
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
Communication between peer layers on different systems is defined by protocols
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1

## Slide 17: What is a Protocol?
Friendly greeting
Time?
12:10 PM
Thanks! Let’s start
Friendly greeting

## Slide 18: What is a Protocol?
Data
An agreement between parties (in the same later) on how to communicate
Defines the syntax of communication
  Header  instructions on how to process payload
  Each protocol defines the format of its headers
    e.g., “the first 32 bits carry the destination address”
Data
Payload
Header

## Slide 19: What is a Protocol?
An agreement between parties on how to communicate
Defines the syntax of communication
And semantics
  “First a hello, then a request…”
  We will study many protocols later in the semester
Protocols exist at many levels, hardware, and software
  Defined by standards bodies like IETF, IEEE, ITU

## Slide 20: Protocols at different layers
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 21: ONE network layer protocol
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 22: Layer encapsulation: Protocol headers
TCP header
IP header
Ethernet
header
HTTP
request/response
User A
User B
Notes: Deepest level most header

## Slide 23: 5-minute break!

## Slide 24: Announcements

## Slide 25: Three steps
Decompose the problem into tasks
Organize these tasks
Assign tasks to entities (who does what)

## Slide 26: What get’s implemented where?
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1

## Slide 27: What gets implemented at the end systems?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 28: What gets implemented in the network?
Bits arrive on wire  physical layer (L1)
Packets must be delivered across links and local networks  datalink layer (L2)
Packets must be delivered between networks for global delivery  network layer (L3)
The network does not support reliable delivery
  Transport layer (and above) not supported

## Slide 29: Simple Diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 30: A closer look: End system
Application
  Web server, browser, mail, game
Transport and network layer
  typically part of the operating system
Datalink and physical layer
  hardware/firmware/drivers

## Slide 31: What gets implemented in the network?
Bits arrive on wire  physical layer (L1)
Packets must be delivered across links and local networks  datalink layer (L2)
Packets must be delivered between networks for global delivery  network layer (L3)
Switches implement only physical and datalink layers (L1, L2)
Routers implement the network layer too (L1, L2, L3)

## Slide 32: A closer look at the network
switch
link
Internet Service Provider

## Slide 33: A closer look at the network
switch
link
Internet Service Provider
routers
switch

## Slide 34: Switches vs. Routers
Switches do what routers do but don’t participate in global delivery, just local delivery
  Switches only need to support L1, L2
  Routers support L1-L3
Won’t focus on the router/switch distinction
  Almost all boxes support network layer these days

## Slide 35: Logical communication
A layer interact with its peers corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 36: Physical communication
Communication goes down to physical network
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 37: A protocol-centric diagram
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 38: Pros and cons of layering
Why layers?
Reduce complexity
Improve flexibility
Why not?
Higher overheads
Cross-layer information often useful

## Slide 39: IP is the narrow waist of the layering hourglass
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 40: Implications of hourglass
Single network-layer protocol (IP)
Allows arbitrary networks to interoperate
  Any network that supports IP can exchange packets
Decouples applications from low-level networking technologies
  Applications function on all networks
Supports simultaneous innovations above and below IP
But changing IP itself is hard (e.g., IPv4  IPv6)

## Slide 41: Placing network functionality
End-to-end arguments by Saltzer, Reed, and Clark
  Dumb network and smart end systems
  Functions that can be completely and correctly implemented only with the knowledge of application end host, should not be pushed into the network
  Sometimes necessary to break this for performance and policy optimizations
  Fate sharing: fail together or don’t fail at all

## Slide 42: Summary
Layering is a good way to organize networks
Unified Internet layer decouples applications from networks
E2E argument encourages us to keep IP simple