## Slide 1: EECS 489 Computer Networks Fall 2019
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Transport layer basics
UDP
Designing a reliable transport protocol

## Slide 3: Transport layer
Layer at end hosts, between the application and network layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 4: Why a transport layer?
IP addresses capture hosts, but end-to-end communication happens between applications
  Need a way to decide which packets go to which applications (multiplexing/demultiplexing)
IP provides a weak service model (best-effort)
  Packets can be corrupted, delayed, dropped, reordered, duplicated
  No guidance on how much traffic to send and when
  Dealing with this is tedious for application developers

## Slide 5: Multiplexing & demultiplexing
Multiplexing (Mux)
  Gather and combining data chunks at the source from different applications and delivering to the network layer
Demultiplexing (Demux)
  Delivering correct data to corresponding sockets from a multiplexed stream

## Slide 6: Role of the transport layer
Communication between processes
  Mux and demux from/to application processes
  Implemented using ports

## Slide 7: Role of the transport layer
Communication between processes
Provide common end-to-end services for app layer [optional]
  Reliable, in-order data delivery
  Well-paced data delivery
    Too fast may overwhelm the network
    Too slow is not efficient

## Slide 8: Role of the transport layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
  Also SCTP, MPTCP, SST, RDP, DCCP, …
Notes: SCTP: Stream Control Transmission Protocol
MPTCP: Multipath TCP
SST: Structured Stream Transport
RDP: Remote Desktop Protocol
DCCP: Datagram Congestion Control Protocol

## Slide 9: Role of the transport layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist transport protocol
  Only provides mux/demux capabilities

## Slide 10: Role of the transport layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist transport protocol
  TCP offers a reliable, in-order, byte stream abstraction
  With congestion control, but w/o performance guarantees (delay, b/w, etc.)

## Slide 11: Applications and sockets
Socket: software abstraction for an application process to exchange network messages with the (transport layer in the) operating system
Two important types of sockets
  UDP socket: TYPE is SOCK_DGRAM
  TCP socket: TYPE is SOCK_STREAM

## Slide 12: Ports
16-bit numbers that help distinguishing apps
  Packets carry src/dst port no in transport header
  Well-known (0-1023) and ephemeral ports
OS stores mapping between sockets and ports
  Port in packets and sockets in OS
  For UDP ports (SOCK_DGRAM)
    OS stores (local port, local IP address)  socket
  For TCP ports (SOCK_STREAM)
    OS stores (local port, local IP, remote port, remote IP)  socket

## Slide 13: UDP: User Datagram Protocol
Lightweight communication between processes
  Avoid overhead and delays of order & reliability
UDP described in RFC 768 – (1980!)
  Destination IP address and port to support demultiplexing
SRC port
DST port
Length
Checksum
DATA

## Slide 14: UDP (cont’d)
Optional error checking on the packet contents
  (checksum field = 0 means “don’t verify checksum”)
Source port is also optional
  Useful to respond back to the sender in some cases

## Slide 15: Why a transport layer?
IP packets are addressed to a host but end-to-end communication is between application processes at hosts
  Need a way to decide which packets go to which applications (mux/demux)
IP provides a weak service model (best-effort)
  Packets can be corrupted, delayed, dropped, reordered, duplicated
  No guidance on how much traffic to send and when
  Dealing with this is tedious for application developers

## Slide 16: Reliable transport
@Sender
  Send packets
@Receiver
  Wait for packets
In a perfect world, reliable transport is easy

## Slide 17: Reliable transport
In a perfect world, reliable transport is easy
All the bad things best-effort can do
  A packet is corrupted (bit errors)
  A packet is lost (why?)
  A packet is delayed (why?)
  Packets are reordered (why?)
  A packet is duplicated (why?)

## Slide 18: Dealing with packet corruption
Time
Sender
Receiver
1
2
2


ack
nack

## Slide 19: Dealing with packet corruption
Time
Sender
Receiver
1
1


ack(1)
ack(1)
What if the ACK/NACK is corrupted?
Packet #1 or #2?
2
P(2)
P(1)
P(1)
Data and ACK packets carry sequence numbers

## Slide 20: Dealing with packet loss
Time
Sender
Receiver
1
1

ack(1)
P(1)
P(1)
Timer-driven loss detection Set timer when packet is sent; retransmit on timeout
Timeout
P(2)

## Slide 21: Dealing with packet loss (of ack)
Time
Sender
Receiver
1
1

ack(1)
P(1)
P(1)
Timeout
P(2)
duplicate!

## Slide 22: Dealing with delay
Time
Sender
Receiver
1
.
.
.
1
ack(1)
P(1)
P(1)
Timer-driven retransmission can lead to duplicates
Timeout
P(2)
duplicate!
ack(1)

## Slide 23: Components of a solution
Checksums (to detect bit errors)
Timers (to detect loss)
Acknowledgements (positive or negative)
Sequence numbers (to deal with duplicates)

## Slide 24: 5-minute break!

## Slide 25: Designing a reliable transport

## Slide 26: A Solution: “Stop and Wait”
A correct reliable transport protocol, but an extremely inefficient one
@Sender
  Send packet(I); (re)set timer; wait for ack
  If (ACK)
    I++; repeat
  If (NACK or TIMEOUT)
    repeat
@Receiver
  Wait for packet
  If packet is OK, send ACK
  Else, send NACK
  Repeat

## Slide 27: Stop & Wait is inefficient
ACK
DATA
Sender
Receiver
RTT
If (TRANS << RTT) then
Throughput ~ DATA/RTT
TRANS

## Slide 28: Orders of magnitude
Transmission time for 10Gbps link:
  ~ microsecond for 1500 byte packet
RTT:
  1,000 kilometers ~ O(10) milliseconds

## Slide 29: Three design decisions
Which packets can sender send?
How does receiver ack packets?
Which packets does sender resend?

## Slide 30: Sliding window
Window = set of adjacent sequence numbers
  The size of the set is the window size; assume window size is n
General idea: send up to n packets at a time
  Sender can send packets in its window
  Receiver can accept packets in its window
  Window of acceptable packets “slides” on successful reception/acknowledgement
  Window contains all packets that might still be in transit
Sliding window often called “packets in flight”

## Slide 31: Sliding window
Let A be the last ack’d packet of sender without gap; then window of sender = {A+1, A+2, …, A+n}
Let B be the last received packet without gap by receiver, then window of receiver = {B+1,…, B+n}
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
n
A
Already ACK’d
Sent but not ACK’d
Cannot be sent
sequence number 

## Slide 32: Throughput of sliding window
If window size is n, then throughput is roughly
  MIN(n*DATA/RTT, Link Bandwidth)
Compare to Stop and Wait: Data/RTT
What happens when n gets too large?

## Slide 33: Acknowledgements w/ sliding window
Two common options
  Cumulative ACKs: ACK carries next in-order sequence number that the receiver expects

## Slide 34: Cumulative acknowledgements
At receiver
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
After receiving B+1, B+2
n
Bnew= B+2
Receiver sends ACK(B+3) = ACK(Bnew+1)

## Slide 35: Cumulative acknowledgements (cont’d)
At receiver
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
After receiving B+4, B+5
n
B
Receiver sends ACK(B+1)

## Slide 36: Acknowledgements w/ sliding window
Two common options
  Cumulative ACKs: ACK carries next in-order sequence number the receiver expects
  Selective ACKs: ACK individually acknowledges correctly received packets
Selective ACKs offer more precise information but require more complicated book-keeping

## Slide 37: Sliding window protocols
Resending packets: two canonical approaches
  Go-Back-N
  Selective Repeat
Many variants that differ in implementation details

## Slide 38: Go-Back-N (GBN)
Sender transmits up to n unacknowledged packets
Receiver only accepts packets in order
  Discards out-of-order packets (i.e., packets other than B+1)
Receiver uses cumulative acknowledgements
  i.e., sequence# in ACK = next expected in-order sequence#
Sender sets timer for 1st outstanding ack (A+1)
If timeout, retransmit A+1, … , A+n

## Slide 39: Sliding window with GBN
Let A be the last ack’d packet of sender without gap; then window of sender = {A+1, A+2, …, A+n}
Let B be the last received packet without gap by receiver, then window of receiver = {B+1,…, B+n}
n
A
Already ACK’d
Sent but not ACK’d
Cannot be sent
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
sequence number 

## Slide 40: GBN example w/o errors
Time
Window size = 3 packets
Sender
Receiver
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Sender Window
Receiver Window
6
{4, 5, 6}
.
.
.
.
.
.

## Slide 41: GBN example with errors
Time
Window size = 3 packets
Sender
Receiver
Sender Window
Receiver Window
1
2
3
4
5
Timeout
Packet 4
6
4
5
6
Discard
Discard

## Slide 42: Selective Repeat (SR)
Sender: transmit up to n unacknowledged packets
Assume packet k is lost, k+1 is not
  Receiver: indicates packet k+1 correctly received
  Sender: retransmit only packet k on timeout
Efficient in retransmissions but complex book-keeping
  Need a timer per packet

## Slide 43: SR example with errors
Window size = 3 packets
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Sender Window
Receiver Window
6
{4, 5, 6}
ACK=5
ACK=6
{4, 5, 6}
{4, 5, 6}
Timeout
Packet 4
4
ACK=4
7
{7, 8, 9}
Sender
Receiver
Buffered
Buffered

## Slide 44: GBN vs. Selective Repeat
When would GBN be better?
  When error rate is low; wastes bandwidth otherwise
When would SR be better?
  When error rate is high; otherwise, too complex

## Slide 45: Observations
For a large-enough window, it is possible to fully utilize a link with sliding windows
Sender has to buffer all unacknowledged packets, because they may require retransmission
Receiver may be able to accept out-of-order packets, but only up to its buffer limits
Implementation complexity depends on protocol details (GBN vs. SR)

## Slide 46: Components of a solution
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments
  Cumulative
  Selective
Sequence numbers (duplicates, windows)
Sliding windows (for efficiency)
Reliability protocols use the above to decide when and what to retransmit or acknowledge

## Slide 47: Summary
Transport layer allows applications to communicate with each other
Provides unreliable and reliable mechanisms
Possible to build reliable transport over unreliable medium
Next lecture
  TCP