## Slide 1: EECS 489 Computer Networks Winter 2017
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
IP routers
Router-assisted congestion control

## Slide 3: IP routers
Core building block of the Internet infrastructure
$120B+ industry
Vendors: Cisco, Huawei, Juniper, Alcatel-Lucent (account for >90%)

## Slide 4: Router definitions
Router capacity = N x R
N = Number of external router “ports”
R = Speed (“line rate”) of a port

## Slide 5: Networks and routers
AT&T
BBN
NYU
UMICH
core
core
edge (ISP)
edge (enterprise)
home, small business
Notes: Bunch of different kinds of routers: small for homes, routers that connect different ISPs or ISPs to enterprises (edge)

## Slide 6: Many types of routers
Core
  R = 10/40/100 Gbps
  NR = O(100) Tbps (Aggregated)
Edge
  R = 1/10/40
  NR = O(100) Gbps
Small business
  R = 10/100/1000 Mbps
  NR < 10 Gbps

## Slide 7: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Control Plane
Data Plane

## Slide 8: What’s inside a router?
Linecards
  Input linecards process packets on their way in
  Output linecards process packets on way out
  Input and output for the same port are on the same physical linecard
Interconnect/switching fabric
  Transfers packets from input to output ports

## Slide 9: Input linecards
Tasks
  Receive incoming packets (physical layer stuff)
  Update the IP header
    TTL, Checksum, Options and Fragment (maybe)
  Lookup the output port for the destination IP address
  Queue the packet at the switch fabric
Challenge: speed!
  100B packets @ 40Gbps  new packet every 20 nano secs!
  Typically implemented with specialized ASICs (network processors)
Notes: Next: one particular part of the functionality: how to determine the output port for the destination IP address

## Slide 10: Looking up the output port
One entry for each address  4 billion entries!
For scalability, addresses are aggregated
Notes: How does a router determine which output port for the packet!

## Slide 11: Example
Router with 4 ports
Destination address range mapping
  11 00 00 00 to 11 00 00 11: Port 1
  11 00 01 00 to 11 00 01 11: Port 2
  11 00 10 00 to 11 00 11 11: Port 3
  11 01 00 00 to 11 01 11 11: Port 4

## Slide 12: Example
Router with 4 ports
Destination address range mapping
  11 00 00 00 to 11 00 00 11: Port 1
  11 00 01 00 to 11 00 01 11: Port 2
  11 00 10 00 to 11 00 11 11: Port 3
  11 01 00 00 to 11 01 11 11: Port 4

## Slide 13: Longest prefix matching
110000**
110001**
1100****
1101****
ISP Router
Port 1
Port 2
Port 3
Port 4

## Slide 14: Finding match efficiently
Testing each entry to find a match scales poorly
  On average: O(number of entries)
Leverage tree structure of binary strings
  Set up tree-like data structure

## Slide 15: Longest prefix matching
110000**
110001**
1100****
1101****
ISP Router
Port 1
Port 2
Port 3
Port 4

## Slide 16: Tree structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
000  Port 1
001  Port 2
0**  Port 3
1**  Port 4
Notes: Idea: build tree to help with match. When a new packet comes in, walk the tree to determine the correct port.
Each level in the tree: one bit. Root: all wild cards

## Slide 17: Tree structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
000  Port 1
001  Port 2
0**  Port 3
1**  Port 4
Record port associated with latest match, and only override when it matches another prefix during walk down tree
Notes: Idea: build tree to help with match. When a new packet comes in, walk the tree to determine the correct port.
Each level in the tree: one bit. Root: all wild cards

## Slide 18: Input linecards
Main challenge is processing speeds
Tasks involved:
  Update packet header (easy)
  LPM lookup on destination address (harder)
Mostly implemented with specialized hardware

## Slide 19: Output linecards
Packet classification: map packets to flows
Buffer management: decide when and which packet to drop
Scheduler: decide when and which packet to transmit
Scheduler
flow 1
flow 2
flow n
Classifier
Buffer management

## Slide 20: Simplest: FIFO router
No classification
Drop-tail buffer management: when buffer is full drop the incoming packet
First-In-First-Out (FIFO) Scheduling: schedule packets in the same order they arrive
Scheduler
Buffer

## Slide 21: Packet classification
Classify an IP packet based on a number of fields in the packet header, e.g.,
  Source/destination IP address (32 bits)
  Source/destination TCP port number (16 bits)
  Type of service (TOS) byte (8 bits)
  Type of protocol (8 bits)
In general fields are specified by range
  Classification requires a multi-dimensional range search!

## Slide 22: Scheduler
One queue per “flow”
Scheduler decides when and from which queue to send a packet
Goals of a scheduling algorithm
  Fast!
  Depends on the policy being implemented (fairness, priority, etc.)

## Slide 23: Priority scheduler
Priority
Scheduler
Priority scheduler: packets in the highest priority queue are always served before the packets in lower priority queues
High priority
Medium priority
Low priority

## Slide 24: Round-robin scheduler
Round robin: packets are served from each queue in turn
Fair queuing (FQ): round-robin for packets of different size
Weighted fair queueing (WFQ): serve proportional to weight
  FQ gives equal weight to each flow

## Slide 25: Connecting inputs to outputs: Switching fabric
Mini-network
Three primary ways to switch
  Switching via shared memory
  Switching via a bus
  Switching via an inter-connection network
    For example, cross-bar

## Slide 26: Context
Crossbar fabric
Centralized scheduler
Input ports
Output ports

## Slide 27: Scheduling
Run links at full capacity, fairness across inputs
Scheduling formulated as finding a matching on a bipartite graph
Practical solutions look for a good maximal matching (fast)
Input ports
Output ports

## Slide 28: 5-minute break!

## Slide 29: Announcements
Midterm on Wednesday, Feb 22
  No office hours; grading!
Assignment 2 is due at the end of next week
Today is the last day for submitting midterm teaching evaluation

## Slide 30: Router-assisted Congestion control

## Slide 31: Recap: TCP problems
Misled by non-congestion losses
Fills up queues leading to high delays
Short flows complete before discovering available capacity
AIMD impractical for high speed links
Saw tooth discovery too choppy for some apps
Unfair under heterogeneous RTTs
Tight coupling with reliability mechanisms
End hosts can cheat
Routers tell endpoints if they’re congested
Routers tell endpoints what rate to send at
Routers enforce fair sharing
Could fix many of these with some help from routers!

## Slide 32: Router-assisted congestion control
Three tasks for congestion control
  Isolation/fairness
  Adjustment
  Detecting congestion

## Slide 33: Fairness: General approach
Routers classify packets into “flows”
  Let’s assume flows are TCP connections
Each flow has its own FIFO queue in router
Router services flows in a fair fashion
  When line becomes free, take packet from next flow in a fair order
What does “fair” mean exactly?

## Slide 34: Max-Min fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
  ai = min(f, ri)
  where f is the unique value such that Sum(ai) = C
r1
r2
r3
?
?
?
C bits/s

## Slide 35: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  r3’s need is only 2
    Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 36: Max-Min fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
  ai = min(f, ri)
  where f is the unique value such that Sum(ai) = C
If you don’t get full demand, no one gets more than you
This is what round-robin service gives if all packets are the same size

## Slide 37: How do we deal with packets of different sizes?
Mental model: Bit-by-bit round robin (“fluid flow”)
Can you do this in practice?
  No, packets cannot be preempted
But we can approximate it
  This is what “fair queuing” routers do

## Slide 38: Fair Queuing (FQ)
For each packet, compute the time at which the last bit of a packet would have left the router if flows are served bit-by-bit
Then serve packets in the increasing order of their deadlines

## Slide 39: Example
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrival traffic)
Flow 2
(arrival traffic)
Service
in fluid flow
system
FQ Packet
system
time
time
time
time

## Slide 40: Fair Queuing (FQ)
Implementation of round-robin generalized to the case where not all packets are equal sized
Weighted fair queuing (WFQ): assign different flows different shares
Today, some form of WFQ implemented in almost all routers
  Not the case in the 1980-90s, when CC was being developed
  Mostly used to isolate traffic at larger granularities (e.g., per-prefix)

## Slide 41: FQ vs. FIFO
FQ advantages:
  Isolation: cheating flows don’t benefit
  Bandwidth share does not depend on RTT
  Flows can pick any rate adjustment scheme they want
Disadvantages:
  More complex than FIFO: per flow queue/state, additional per-packet book-keeping

## Slide 42: FQ in the big picture
FQ does not eliminate congestion  it just manages the congestion
1Gbps
100Mbps
1Gbps
5Gbps
1Gbps
Blue and Green get 0.5Gbps; any excess will be dropped
Will drop an additional 400Mbps from the green flow
If the green flow doesn’t drop its sending rate to 100Mbps, we’re wasting 400Mbps that could be usefully given to the blue flow

## Slide 43: FQ in the big picture
FQ does not eliminate congestion  it just manages the congestion
  Robust to cheating, variations in RTT, details of delay, reordering, retransmission, etc.
But congestion (and packet drops) still occurs
We still want end-hosts to discover/adapt to their fair share!
What would the end-to-end argument say w.r.t. congestion control?

## Slide 44: Fairness is a controversial goal
What if you have 8 flows, and I have 4?
  Why should you get twice the bandwidth?
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Why shouldn’t you be penalized for using more scarce bandwidth?
What is a flow anyway?
  TCP connection
  Source-Destination pair?
  Source?

## Slide 45: Router-Assisted Congestion Control
CC has three different tasks:
  Isolation/fairness
  Rate adjustment
  Detecting congestion

## Slide 46: Why not let routers tell what rate end hosts should use?
Packets carry “rate field”
Routers insert “fair share” f in packet header
End-hosts set sending rate (or window size) to f
  Hopefully (still need some policing of end hosts!)
This is the basic idea behind the “Rate Control Protocol” (RCP) from Dukkipati et al. ’07
  Flows react faster

## Slide 47: Router-Assisted Congestion Control
CC has three different tasks:
  Isolation/fairness
  Rate adjustment
  Detecting congestion

## Slide 48: Explicit Congestion Notification (ECN)
Single bit in packet header; set by congested routers
  If data packet has bit set, then ACK has ECN bit set
Many options for when routers set the bit
  Tradeoff between (link) utilization and (packet) delay
Congestion semantics can be exactly like that of drop
  i.e., end-host reacts as though it saw a drop

## Slide 49: ECN
Advantages:
  Don’t confuse corruption with congestion; recovery w/ rate adjustment
  Can serve as an early indicator of congestion to avoid delays
  Easy (easier) to incrementally deploy
    Today: defined in RFC 3168 using ToS/DSCP bits in the IP header
    Common in datacenters

## Slide 50: One final proposal: Charge people for congestion!
Use ECN as congestion markers
Whenever I get an ECN bit set, I have to pay $$
Now, there’s no debate over what a flow is, or what fair is…
Idea started by Frank Kelly at Cambridge
  “Optimal” solution, backed by much math
  Great idea: simple, elegant, effective
  Unclear that it will impact practice

## Slide 51: Summary
IP routers form the backbone of the Internet
Aims for speed while providing fairness
Routers can assist in addressing/mitigating many of TCP’s shortcomings
Next week: Midterm review and the Midterm