## Slide 1: EECS 489 Computer Networks Winter 2024
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Logistics
Open book/text/notes, but OFFLINE
  Except for taking the exam over the Internet
You’re NOT allowed to write/run any programs
You’re NOT allowed to collaborate with anyone
You’re NOT allowed to use any AI

## Slide 3: General guidelines (1)
Test only assumes material covered in lecture, discussion sections, quizzes, and assignments
  Text: only to clarify details and context for the above
The test doesn’t require you to do complicated calculations
  Use this as a hint to determine if you’re on right track
You don’t need to memorize anything
You do need to understand how things work

## Slide 4: General guidelines (2)
Be prepared to:
  Weigh design options outside of the context we studied them in
  Contemplate new designs we haven’t covered in detail but can be put together
    e.g., I introduce a new IP address format; how does this affect..”
  Reason from what you know about the pros/cons of solutions we did study

## Slide 5: General guidelines (3)
Exam format
  Q1: True-False questions
  Q2: MCQ questions
  Q3-QN networking use cases
    Questions not ordered in terms of complexity
60 minutes

## Slide 6: This review
Walk through what you’re expected to know at this point: key topics, important aspects of each
Not covered in review does NOT imply you don’t need to know it
  But if it’s covered today, you should know it
Summarize, not explain
  Stop me when you want to discuss something further!

## Slide 7: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming, and Cloud
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lecture 10–11)
  Overview
  Data plane

## Slide 8: Basic concepts
You should know:
  Packet vs. circuit switching
  Statistical multiplexing
  Link characteristics
  Packet delays

## Slide 9: Switched networks
End-systems and networks connected by switches instead of directly connecting them
Allows us to scale
  For example, directly connecting N nodes to each other would require N2 links!

## Slide 10: Two approaches to sharing
Packet switching
  Network resources consumed on demand per-packet
  Admission control: per packet
Circuit switching
  Network resources reserved a priori at “connection” initiation
  Admission control: per connection

## Slide 11: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Good for bursty traffic (average << peak demand)
  Packet switching exploits statistical multiplexing better than circuit switching

## Slide 12: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 13: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation
We only consider store-and-forward in this class

## Slide 14: What we want
http://123.xyz
123.xyz server

## Slide 15: (Some of) What happens…
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 16: (More of) What happens
5.6.7.*
host
host
host
...
5.6.7.8
1.2.3.*
host
host
DNS
...
router
router
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 17: What we get
http://123.xyz
123.xyz server
Hello

## Slide 18: Layers
Layer: a part of a system with well-defined interfaces to other parts
One layer interacts only with layer above and layer below
Two layers interact only through the interface between them

## Slide 19: Layers in practice
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 20: Layer encapsulation: Protocol headers
TCP header
IP header
Ethernet
header
HTTP
request/response
User A
User B
Notes: Deepest level most header

## Slide 21: IP is the narrow waist of the layering hourglass
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 22: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming, and Cloud
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lecture 10–11)
  Overview
  Data plane

## Slide 23: Hyper Text Transfer Protocol (HTTP)
Client-server architecture
  Server is “always on” and “well known”
  Clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format
  Before HTTP/2

## Slide 24: Object request response time
RTT (round-trip time)
  Time for a small packet to travel from client to server and back
Response time
  1 RTT for TCP setup
  1 RTT for HTTP request and first few bytes
  Transmission time
  Total = 2RTT + Transmission Time
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
RTT
RTT
Tx

## Slide 25: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent connections
  Parallel/concurrent connections
  Pipelined transfers over the same connection
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 26: Scorecard: Getting n small objects
Time dominated by latency
One-at-a-time: ~2n RTT
m concurrent: ~2[n/m] RTT
Persistent: ~ (n+1) RTT
Pipelined: ~2 RTT
Pipelined and Persistent: ~2 RTT first time; RTT later for another n from the same site

## Slide 27: Scorecard: Getting n large objects each of size F
Time dominated by TCP throughput BC (<= BL), where bottleneck link bandwidth is BL
  Assuming all TCP connections go through the same bottleneck link
One-at-a-time: ~ nF/BC
m concurrent: ~ nF/(mB’C)
  Assuming each TCP connection gets the same throughput (B’C), where mB’C <= BL
Pipelined and/or persistent: ~ nF/BC
  The only thing that helps is higher throughput

## Slide 28: Content Distribution Networks (CDN)
Caching and replication as a service
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)

## Slide 29: Hierarchies in the DNS
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 30: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers

## Slide 31: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 32: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 33: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 34: Name resolution: Recursive
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 35: Name resolution: Iterative
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?

## Slide 36: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.google.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 37: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while to minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 38: DASH : Dynamic Adaptive Streaming over HTTP
Keep multiple resolutions of the same video
  Stored in a manifest file in the HTTP server
Client asks for the manifest file first to learn about the options
Asks for chunks at a time and measures available bandwidth while they are downloaded
  Low bandwidth ⇒ switch to lower bitrate
  High bandwidth ⇒ switch to higher bitrate

## Slide 39: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 40: Traditional datacenter networks
Rack
Aggregation
Core

## Slide 41: Challenges
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers’ bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 42: Modern datacenter networks: More bandwidth, more paths
Rack
Aggregation
Core

## Slide 43: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 44: 5-minute break!

## Slide 45: Announcements
60-minute midterm exam on canvas
  Mar 6
  Available from 9:30AM
  You MUST start before 11AM
Please fill up midterm teaching evaluation

## Slide 46: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming, and Cloud
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lecture 10–11)
  Overview
  Data plane

## Slide 47: Role of the transport layer
(1) Communication between application processes
  Mux and demux from/to application processes
  Implemented using ports
(2) Provide common end-to-end services for app layer
  Reliable, in-order data delivery
  Well-paced data delivery

## Slide 48: UDP vs. TCP
 | UDP | TCP
Data abstraction | Packets (datagrams) | Stream of bytes of arbitrary length
Service | Best-effort (same as IP) | Reliability In-order delivery Congestion control Flow control
  Both UDP and TCP perform mux/demux via ports

## Slide 49: Reliable transport: General concepts
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments (feedback from receiver)
  Cumulative: “received everything up to X”
  Selective: “received X”
Sequence no (detect duplicates, accounting)
Sliding windows (for efficiency)
You should know:
what these concepts are
why they exist
how TCP uses them

## Slide 50: Designing a reliable transport protocol
Stop and wait is correct but inefficient
  Works packet by packet (of size DATA)
  Throughput is (DATA/ RTT)
Sliding window: use pipelining to increase throughput
  n packets at a time results in higher throughput
  MIN(n*DATA/RTT, Link Bandwidth)

## Slide 51: The TCP abstraction
TCP delivers a reliable, in-order, byte stream
Reliable: TCP resends lost packets (recursively)
  Until it gives up and shuts down connection
In-order: TCP only hands consecutive chunks of data to application
Byte stream: TCP assumes there is an incoming stream of data, and attempts to deliver it to app

## Slide 52: Things to know about TCP
How TCP achieves reliability
RTT estimation
Connection establishment/teardown
Flow Control
Congestion Control (concepts only)
For each, know how the functionality is implemented and why it is needed

## Slide 53: Reliability
Having TCP take care of it simplifies application development
How
  Checksums and timers (for error and loss detection)
  Fast retransmit (to detect faster-than-timeout loss)
  Cumulative ACKs (receiver feedback: what’s lost?)
  Sliding windows (for efficiency)
  Buffers at sender (hold packets until ACKs arrive)
  Buffers at receiver (to reorder packets before delivery to application)

## Slide 54: Establishing/terminating a TCP connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
Three-way handshake to terminate (normal operation)
SYN
SYN ACK
ACK
A
B
Data
Data

## Slide 55: Flow control
Why?
  TCP at the receiver must buffer a packet until all packets before it (in byte-order) have arrived and the receiving application has consumed available bytes
  Hence, receiver advances its window when the receiving application consumes data
  Sender advances its window when new data ACK’d
  Risk of sender overrunning the receiver’s buffers
How?
  “Advertised Window” field in TCP header

## Slide 56: Congestion control
Why?
  Because the network itself can be the bottleneck
  Should make efficient use of available network capacity
    While sharing available capacity fairly with other flows
    And adapting to changes in available capacity
How?
  Dynamically adapts the size of the sending window

## Slide 57: Put together
Flow Control
  Restrict window to RWND to make sure that the receiver isn’t overwhelmed
Congestion Control
  Restrict window to CWND to make sure that the network isn’t overwhelmed
Together
  Restrict window to min{RWND, CWND} to make sure that neither the receiver nor the network are overwhelmed

## Slide 58: CC implementation
States at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
  dupACKcount and timer
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 59: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence, after one RTT with no drops: CWND = 2xCWND

## Slide 60: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence, after one RTT with no drops: CWND = CWND + 1
Congestion avoidance phase

## Slide 61: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 62: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 63: Example
t
Window
Slow-start restart: Go back to CWND = 1 MSS, but take advantage of knowing the previous value of CWND
Slow start in operation until it reaches half of previous CWND, i.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 64: TCP flavors
TCP-Tahoe
  CWND =1 on 3 dupACKs
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on 3 dupACKs
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  Incorporates selective acknowledgements

## Slide 65: A simple model for TCP throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 66: A simple model for TCP throughput
in MSS
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 67: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming, and Cloud
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lecture 10–11)
  Overview
  Data plane

## Slide 68: Network layer
Present everywhere
Performs addressing, forwarding, and routing, among other tasks
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 69: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm

## Slide 70: Forwarding
umich.edu
mit.edu
111010010
MIT
#1
#2
#3
#4
Destination | Next Hop
UMICH | 1
UCB | 3
MIT | 2
NYU | 4
Forwarding Table

## Slide 71: Designing the IP header
Think of the IP header as an interface
  Between the source and destination end-systems
  Between the source and network (routers)
Designing an interface
  What task(s) are we trying to accomplish?
  What information is needed to do it?
Header reflects information needed for basic tasks

## Slide 72: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  Loops: TTL (8 bits)
  Corruption: checksum (16 bits)
  Packet too large: fragmentation fields (32 bits)

## Slide 73: IPv4 and IPv6 header comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
128-bit Source Address |  |  |  | 
128-bit Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 74: Philosophy of changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation and checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 75: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Control Plane
Data Plane

## Slide 76: Input linecards
Main challenge is processing speeds
Tasks involved:
  Update packet header (easy)
  LPM lookup on destination address (harder)
Mostly implemented with specialized hardware

## Slide 77: Looking up the output port
One entry for each address  4 billion entries!
For scalability, addresses are aggregated
Notes: How does a router determine which output port for the packet!

## Slide 78: Longest prefix matching
110000**
110001**
1100****
1101****
ISP Router
Port 1
Port 2
Port 3
Port 4
Send to the port with the longest prefix match

## Slide 79: Tree structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
000  Port 1
001  Port 2
0**  Port 3
1**  Port 4
Record port associated with latest match, and only override when it matches another prefix during walk down tree
Notes: Idea: build tree to help with match. When a new packet comes in, walk the tree to determine the correct port.
Each level in the tree: one bit. Root: all wild cards

## Slide 80: Output linecards
Packet classification: map packets to flows
Buffer management: decide when and which packet to drop
Scheduler: decide when and which packet to transmit
Scheduler
flow 1
flow 2
flow n
Classifier
Buffer management

## Slide 81: Crossbar interconnect
2N buses intersecting with each other:
  N input
  N output
Non-blocking
Input ports
Output ports
Notes: Non-blocking: Packets being forwarded to different output ports does not block each other.

## Slide 82: Max-Min fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
  ai = min(f, ri)
  where f is the unique value such that Sum(ai) = C
r1
r2
r3
?
?
?
C bits/s
Notes: If you don’t get full demand, no one gets more than you.

## Slide 83: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  r3 needs only 2
    Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 84: Max-Min fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
  ai = min(f, ri)
  where f is the unique value such that Sum(ai) = C
If you don’t get full demand, no one gets more than you
This is what round-robin service gives if all packets are the same size

## Slide 85: Summary
Demo Exam on Canvas