## Slide 1: EECS 489 Computer Networks Fall 2021
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Logistics
Open book/text/notes, but OFFLINE
  Except for taking the exam over the Internet
You’re NOT allowed to write/run any programs
You’re NOT allowed to collaborate with anyone

## Slide 3: General guidelines (1)
Test only assumes material covered in lecture, sections, and assignments after midterm
  Text: only to clarify details and context for the above
The test doesn’t require you to do complicated calculations
  Use this as a hint to determine if you’re on right track
You don’t need to memorize anything
You do need to understand how things work

## Slide 4: General guidelines (2)
Be prepared to:
  Weigh design options outside of the context we studied them in
  Contemplate new designs we haven’t covered in detail but can be put together
    e.g., I introduce a new IP address format; how does this affect..”
  Reason from what you know about the pros/cons of solutions we did study

## Slide 5: General guidelines (3)
Exam format
  Like midterm, but we’re working to avoid cascading mistakes
Questions not ordered in terms of complexity
    Read all carefully
Pace yourself accordingly!

## Slide 6: This review
Walk through what you’re expected to know since the midterm: key topics, important aspects of each
Not covered in review does NOT imply you don’t need to know it
  But if it’s covered today, you should know it
Summarize, not explain
  Stop me when you want to discuss something further!

## Slide 7: The networking stack
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Application
End system
Transport
Network
Datalink
Physical
Application
End system
Network
Datalink
Physical
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 8: Topics
Network layer (lectures 12–16)
  Intra-domain routing
  Inter-domain routing
  SDN
Link layer (lectures 17–19)
  Ethernet
  Wireless
Datacenter networking (lectures 20)

## Slide 9: Network layer
Present everywhere
Performs addressing, forwarding, and routing, among other tasks
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 10: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm
Very different timescales!

## Slide 11: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Control Plane
Data Plane

## Slide 12: Routing: Local vs. global view
Local routing state is the forwarding table in a single router
  By itself, the state in a single router cannot be evaluated
  It must be evaluated in terms of the global context
Global state refers to the collection of forwarding tables in each of the routers
  Global state determines which paths packets take

## Slide 13: “Valid” routing state
Global state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
Goal of routing protocols: compute valid state
  How can we tell if routing state if valid?
Notes: What could go wrong?

## Slide 14: Necessary and sufficient condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing link (next-hop)
  A packet arrives, but the forwarding decision does not yield any outgoing link
A loop is when a packet cycles around the same set of nodes forever

## Slide 15: Least-cost routes
Least-cost routes provide an easy way to avoid loops
  No reasonable cost metric is minimized by traversing a loop
Least-cost paths form a spanning tree for each destination rooted at that destination

## Slide 16: Intra-domain routing
Link-state (LS) routing protocol
  Dijkstra’s algorithm
  Broadcast neighbors’ info to everyone
Distance vector (DV) routing protocol
  Bellman-Ford algorithm
  Gossip to neighbors about everyone

## Slide 17: Similarities between LS and DV routing
Both are shortest-path based routing
  Minimizing cost metric (link weights) a common optimization goal
    Routers share a common view as to what makes a path “good” and how to measure the “goodness” of a path
Due to shared goal, commonly used inside an organization
  RIP and OSPF are mostly used for intra-domain routing

## Slide 18: Comparison of LS and DV routing
Messaging complexity
LS: with N nodes, E links, O(NE) messages sent
DV: exchange between neighbors only
Speed of convergence
LS: relatively fast
DV: convergence time varies
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes its own table
DV:
  Node can advertise incorrect path cost
  Each node’s table used by others (errors propagate)

## Slide 19: Addressing is key to scalable inter-domain routing
Ability to aggregate addresses is crucial for
  State: Small forwarding tables at routers
    Much less than the number of hosts
  Churn: Limited rate of change in routing tables

## Slide 20: Classful addressing
Three classes
  8-bit network prefix (Class A),
  16-bit network prefix (Class B), or
  24-bit network prefix (Class C)
Example: an organization needs 500 addresses.
  A single class C address is not enough (<500 hosts)
  Instead, a class B address is allocated (~65K hosts)
    Huge waste!

## Slide 21: CIDR: Classless inter-domain routing
Flexible division between network and host addresses
Offers a better tradeoff between size of the routing table and efficient use of the IP address space

## Slide 22: Hierarchy in IP addressing
32 bits are partitioned into a prefix and suffix components
Prefix is the network component; suffix is the host component
Inter-domain routing operates on network prefix
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 23: Administrative structure shapes Inter-domain routing
ASes want freedom to pick routes based on policy
ASes want autonomy
ASes want privacy

## Slide 24: Business relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business implications

## Slide 25: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed
ASes provide “transit” between their customers
Peers do not provide transit between other peers

## Slide 26: BGP inspired by Distance-Vector with four differences
Shortest-path routes may not be picked to enforce policy
Path-Vector routing to avoid loops
Selective route advertisement may affect reachability
Routes may be aggregated for scalability

## Slide 27: BGP: Basic idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises (“exports”) its best routes to one or more IP prefixes
Notes: Arrows are routing message

## Slide 28: Policy dictates how routes are “selected” and “exported”
Selection: Which path to use?
  Controls whether/how traffic leaves the network
Export: Which path to advertise?
  Controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 29: Typical export policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common – but not required! – practice)

## Slide 30: Selection using attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 31: eBGP, iBGP, and IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  Distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intra-domain routing protocol
  Provide internal reachability via shortest path
  E.g., OSPF, RIP

## Slide 32: Announcements
Teaching evaluations
  Due by Dec 10
  75% or higher completion rate will result in +1 on the final grade for everyone
    We are only at 37%
Sample final exam on github!
Final slot sign up by Dec 15 11:59PM EST
  https://forms.gle/WBfVY2qsybbzV4ZeA
  Defaults to 8AM EST Dec 20

## Slide 33: “The Power of Abstraction”
“Modularity based on abstraction is the way things get done”
  Barbara Liskov
Abstractions  Interfaces  Modularity

## Slide 34: Separate concerns with abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 35: Traditional fully decentralized control plane
Individual routing algorithm components in every router interact in the control plane
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane

## Slide 36: Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
111010010
MIT
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Control
Plane
Data
Plane
Remote Control

## Slide 37: SDN: Many challenges remain
Hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  Robustness to failures: leverage strong theory of reliable distributed system for control plane
  Security: “baked in” from day one?
Networks, protocols meeting mission-specific requirements
  E.g., real-time, ultra-reliable, ultra-secure
Internet-scaling

## Slide 38: Fixed-function data plane
Traditional switches are fixed-function
  They can do whatever they can do at birth, but they cannot change!
  Bottom-up design
Even OpenFlow was designed to be a fixed protocol
  With a fixed table format
  Capable of doing limited things

## Slide 39: Programmable data plane
What if we could tell switches exactly what we want?
  What table to keep?
  What rules to use?
  What data to keep track of?
  …

## Slide 40: Top-down workflow
Precisely specify using a well-defined language
Compile it down to run on a standardized hardware (e.g., using P4)
Run at line speed

## Slide 41: PISA: Protocol Independent Switch Architecture
Match + Action
Memory
ALU
Programmable
Parser
Programmer declares which
headers are recognized
Programmer declares what
tables are needed and how packets are processed
All stages are identical – makes PISA a good “compiler target”

## Slide 42: Topics
Network layer (lectures 12–16)
  Intra-domain routing
  Inter-domain routing
  SDN
Link layer (lectures 17–19)
  Ethernet
  Wireless
Datacenter networking (lectures 20)

## Slide 43: Data link layer
Provides four primary services
  Framing
    Encapsulates network layer data
  Link access
    Medium access control (MAC) protocol defines when to transmit frames
  Reliable delivery
    Primarily for mediums with high error rates (e.g., wireless)
  Error detection and correction

## Slide 44: Point-to-point vs. broadcast medium
Point-to-point: dedicated pairwise communication
  E.g., long-distance fiber link
  E.g., Point-to-point link b/n Ethernet switch and host
Broadcast: shared wire or medium
  Traditional Ethernet (pre ~2000)
  802.11 wireless LAN

## Slide 45: Random access MAC protocols
When node has packet to send
  Transmit at full channel data rate w/o coordination
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies
  How to detect and recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 46: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does not eliminate all collisions
  Why?

## Slide 47: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired (broadcast) LANs
  Compare transmitted, received signals
Collision detection difficult in wireless LANs
Notes: wireless: because reception while tx is difficult . broadcast isn’t perfect so collisions local

## Slide 48: Limits on CSMA/CD network length
Latency depends on physical length of link
  Time to propagate a frame from one end to other
Suppose A sends a frame at time t
  And B sees an idle line at a time just before t + d
  … so B happily starts transmitting a frame
B detects a collision, and sends jamming signal
  But A cannot see collision until t + 2d
latency d
A
B

## Slide 49: Limits on CSMA/CD network length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  AND keep an eye out for a possible collision
Imposes restrictions; e.g., for 10 Mbps Ethernet
  Maximum length of the wire: 2,500 meters
  Minimum length of a frame: 512 bits (64 bytes)
latency d
A
B

## Slide 50: Why switched Ethernet?
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions and no need for CSMA/CD
  No constraints on link lengths, etc.
Ethernet switch
A
B
C
D

## Slide 51: Ethernet switches are “self learning”
When a packet arrives:
  Inspect source MAC address, associate with incoming port
  Store mapping in the switch table
  Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 52: ARP and DHCP
Link layer discovery protocols
  ARP  Address Resolution Protocol
  DHCP  Dynamic Host Configuration Protocol
  Confined to a single local-area network (LAN)
  Rely on broadcast capability

## Slide 53: Key ideas in both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 54: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Consult the table when sending a packet
  Map dest. IP address to dest. MAC address
  Encapsulate (IP) data packet with MAC header; xmit
What if IP address not in the table?
  Sender broadcasts: Who has IP address 1.2.3.156?
  Receiver replies: MAC address 58-23-D7-FA-20-B0
  Sender caches result in its ARP table

## Slide 55: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 56: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving at destination at slightly different times
  Interference from other sources: Standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
… make communication across (even a point-to-point) wireless link much more “difficult”

## Slide 57: Wireless network characteristics
Multiple wireless senders and receivers create many problems
  Multiple access issues (we’ve seen this before)
  Hidden terminal problem

## Slide 58: Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
Hence, A, C are unaware of their interference at B
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 59: CSMA/CA
Before every data transmission
  Sender sends a Request to Send (RTS) frame with the length of transmission and the destination
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK
If sender doesn’t get a CTS back, it assumes collision
Sender
Receiver
Other node in
sender’s range
RTS
ACK
Data
CTS
Node outside
sender’s range
Notes: 59

## Slide 60: Topics
Network layer (lectures 12–16)
  Intra-domain routing
  Inter-domain routing
  SDN
Link layer (lectures 17–19)
  Ethernet
  Wireless
Datacenter networking (lectures 20)

## Slide 61: Datacenter applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 62: Datacenter traffic characteristics
Two key characteristics
  Most flows are small
  Most bytes come from large flows
Applications want
  High bandwidth (large flows)
  Low latency (small flows)

## Slide 63: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 64: Datacenter networking stack
Networking in modern datacenters
  L2/L3 design
    Addressing / routing / forwarding in the Fat-Tree
  L4 design
    Transport protocol design (w/ Fat-Tree)
  L7 design
    Exploiting application-level information (w/ Fat-Tree)

## Slide 65: Using multiple paths well

## Slide 66: L2/L3 highlights
Load balancing while forwarding
  Per-packet
  Per-flow
Hard-coded addressing or via indirection
Modified LS/DV or source routing

## Slide 67: L4 highlights
Tension between high throughput and low latency requirements
  Deep queues vs shallow queues
DCTCP
  React early, quickly, and with certainty using ECN
  React in proportion to the extent of congestion, not its presence

## Slide 68: L7 highlights
What do applications care about?
  Flow completion time (FCT)
  Coflow completion time (CCT)
    A coflow is a collection of flows with a shared application-level objective
  We should strive to optimize as close an objective as possible to the application

## Slide 69: Summary
THANK YOU SO MUCH!!!