## Slide 1: EECS 489 Computer Networks Fall 2020
Mosharaf Chowdhury
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Datacenter networking

## Slide 3: Recap: Datacenter network requirements
High “bisection bandwidth”
Low latency, even in the worst-case
Large scale
Low cost

## Slide 4: Recap: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 5: “Fat-Tree” topology [SIGCOMM’08]
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 6: Agenda
Networking in modern datacenters
  L2/L3 design
    Addressing / routing / forwarding in the Fat-Tree
  L4 design
    Transport protocol design (w/ Fat-Tree)
  L7 design
    Exploiting application-level information (w/ Fat-Tree)

## Slide 7: Using multiple paths well

## Slide 8: L2/L3 design goals
Routing protocol must expose all available paths
Forwarding must spread traffic evenly over all paths

## Slide 9: Extend DV / LS ?
Routing
  Distance-Vector: Remember all next-hops that advertise equal cost to a destination
  Link-State: Extend Dijkstra’s to compute all equal cost shortest paths to each destination
Forwarding: how to spread traffic across next hops?

## Slide 10: Forwarding
Per-packet load balancing
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 11: Forwarding
Per-packet load balancing
  Traffic well spread (even w/ elephant flows)
  BUT Interacts poorly w/ TCP
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 12: TCP w/ per-packet load balancing
Consider
  Sender sends seq#: 1,2,3,4,5
  Receiver receives: 5,4,3,2,1
  Sender will enter fast retransmit, reduce CWND, retransmit #1, …
  Repeatedly!
Information sharing between multiple paths affects TCP
  One RTT and timeout estimator for multiple paths
  CWND halved when a packet is dropped on any path

## Slide 13: Multipath TCP
Multipath TCP (MPTCP) is an ongoing effort to extend TCP to coexist with multipath routing
  Value beyond datacenters (e.g., spread traffic across WiFi and 4G access)

## Slide 14: Forwarding
Per-flow load balancing (ECMP, “Equal Cost Multi Path”)
  E.g., based on (src and dst IP and port)
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 15: Forwarding
Per-flow load balancing (ECMP)
  A flow follows a single path ( TCP is happy)
  Suboptimal load-balancing; elephants are a problem
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 16: Extend DV / LS ?
How:
  Simple extensions to DV/LS
  ECMP for load balancing
Benefits
  Simple; reuses existing solutions
Problem: poor scaling
  With N destinations, O(N) routing entries and messages
  N now in the millions!

## Slide 17: Solution 1: Topology-aware addressing
10.0.*.*
10.1.*.*
10.2.*.*
10.3.*.*
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 18: Solution 1: Topology-aware addressing
10.0.0.*
10.1.0.*
10.2.0.*
10.3.0.*
10.0.1.*
10.1.1.*
10.2.1.*
10.3.1.*
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 19: Solution 1: Topology-aware addressing
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 20: Solution 1: Topology-aware addressing
10.0.*.*  1
10.1.*.*  2
10.2.*.*  3
10.3.*.*  4
1
2
3
4
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 21: Solution 1: Topology-aware addressing
10.0.0.*  1
10.0.1.*  2
*.*.*.*  3, 4
1
2
3
4
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 22: Solution 1: Topology-aware addressing
10.0.0.*  1
10.0.1.*  2
*.*.*.0  3
*.*.*.1  4
1
2
3
4
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 23: Solution 1: Topology-aware addressing
10.0.0.0  1
10.0.0.1  2
*.*.*.0  3
*.*.*.1  4
1
2
3
4
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 24: Solution 1: Topology-aware addressing
Addresses embed location in regular topology
Maximum #entries/switch: k ( = 4 in example)
  Constant, independent of #destinations!
No route computation / messages / protocols
  Topology is hard-coded, but still need localized link failure detection
Problems?
  VM migration: ideally, VM keeps its IP address when it moves
  Vulnerable to (topology/addresses) misconfiguration
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 25: Solution 2: Centralize + Source routes
Centralized “controller” server knows topology and computes routes
Controller hands server all paths to each destination
  O(#destinations) state per server, but server memory cheap (e.g., 1M routes x 100B/route=100MB)
Server inserts entire path vector into packet header (“source routing”)
  E.g., header=[dst=D | index=0 | path={S5,S1,S2,S9}]
Switch forwards based on packet header
  index++; next-hop = path[index]
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 26: Solution 2: Centralize + Source routes
#entries per switch?
  None!
#routing messages?
  Akin to a broadcast from controller to all servers
Pro:
  Switches very simple and scalable
  Flexibility: end-points control route selection
Cons:
  Scalability / robustness of controller (SDN issue)
  Clean-slate design of everything
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 27: 5-minute break!

## Slide 28: Announcements
Teaching evaluations
  75% or higher completion rate will result in +1 on the final grade for everyone

## Slide 29: Agenda
Networking in modern datacenters
  L2/L3 design
    Addressing / routing / forwarding in the Fat-Tree
  L4 design
    Transport protocol design (w/ Fat-Tree)
  L7 design
    Exploiting application-level information (w/ Fat-Tree)

## Slide 30: Workloads
Partition-Aggregate traffic from user-facing queries
  Numerous short flows with small traffic footprint
  Latency-sensitive
Map-Reduce traffic from data analytics
  Comparatively fewer large flows with massive traffic footprint
  Throughput-sensitive

## Slide 31: Tension between requirements
High throughput
Deep queues at switches
  Queueing delays increase latency
Low latency
Shallow queues at switches
  Bad for bursts and throughput
DCTCP
Objective:
Low Queue Occupancy & High Throughput
Notes: Deep Buffers – bad for latency
Shallow Buffers – bad for bursts & throughput
Reduce RTOmin – no good for latency
AQM – Difficult to tune, not fast enough for incast-style micro-bursts, lose throughput in low stat-mux

## Slide 32: Data Center TCP (DCTCP)
Proposal from Microsoft Research, 2010
  Incremental fixes to TCP for DC environments
  Deployed in Microsoft datacenters (~rumor)
Leverages Explicit Congestion Notification (ECN)

## Slide 33: Recap: Explicit Congestion Notification (ECN)
Defined in RFC 3168 using ToS/DSCP bits in the IP header
Single bit in packet header; set by congested routers
  If data packet has bit set, then ACK has ECN bit set
Routers typically set ECN bit based on average queue length
Congestion semantics exactly like that of drop
  I.e., sender reacts as though it saw a drop

## Slide 34: DCTCP: Key ideas
React early, quickly, and with certainty using ECN
React in proportion to the extent of congestion, not its presence
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%

## Slide 35: Actions due to DCTCP
At the switch
  If instantaneous queue length > k
    Set ECN bit in the packet
At the receiver
  If ECN bit is set in a packet, set ECN bit for its ACK
At the sender
  Maintain an EWMA of the fraction of packets marked (α)
  Adapt window based on α: W ← (1 – α/2) W
  α = 1 implies high congestion: W ← W/2 (like TCP)

## Slide 36: DCTCP: Why it works
React early and quickly: use ECN
  Avoid large buildup in queues  lower latency
React in proportion to the extent of congestion, not its presence
  Maintain high throughput by not over-reacting to congestion
  Reduces variance in sending rates, lowering queue buildups
Still far from ideal

## Slide 37: What’s ideal for a transport protocol?
When the flow is completely transferred?
Latency of each packet in the flow?
Number of packet drops?
Link utilization?
Average queue length at switches?

## Slide 38: Flow Completion Time (FCT)
Time from when flow started at the sender, to when all packets in the flow were received at the receiver

## Slide 39: FCT with DCTCP
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
DCTCP | 1.2777 | 1.5442 | 1.7916 | 2.0476 | 2.3294 | 2.662 | 3.0631 | 3.596
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
Queues are still shared ⇒ Head-of-line blocking

## Slide 40: Solution: Use priorities!
Packets carry a single priority number
  Priority = remaining flow size
Switches
  Very small queues (e.g., 10 packets)
  Send highest-priority/ drop lowest-priority packet
Servers
  Transmit/retransmit aggressively (at full link rate)
  Drop transmission rate only under extreme loss (timeouts)
Provides FCT close to the ideal

## Slide 41: Are we there yet?
Nope!
Someone asked “What do datacenter applications really care about?”
    Someone = Yours truly

## Slide 42: Agenda
Networking in modern datacenters
  L2/L3 design
    Addressing / routing / forwarding in the Fat-Tree
  L4 design
    Transport protocol design (w/ Fat-Tree)
  L7 design
    Exploiting application-level information (w/ Fat-Tree)

## Slide 43: The Map-Reduce Example
Reduce Stage
Map Stage
Observation:
A communication stage cannot complete until all its flows have completed

## Slide 44: Flow-based solutions
GPS
RED
WFQ
CSFQ
ECN
XCP
D2TCP
DCTCP
PDQ
D3
FCP
DeTail
pFabric
2005
2010
2015
1980s
1990s
2000s
RCP
Per-Flow Fairness
Flow Completion Time
Independent flows cannot capture collective communication patterns that are common in data-parallel applications
Notes: All our existing solutions rely on point-to-point flow abstraction.
We have seen hundreds, if not thousands, of proposals to try to address the performance issues using flow as a basic abstraction.
In the early days, it was all about fair allocation.
Recently, as datacenters became more widely used, it’s all about improving flow completion time.
However, flows fundamentally cannot capture the collective communication behavior seen in of data-parallel applications.

## Slide 45: The Coflow abstraction [SIGCOMM’14]
Coflow is a communication abstraction for data-parallel applications to express their performance goals; e.g.,
  Minimize completion times,
  Meet deadlines, or
  Perform fair allocation
Not for individual flows; for entire stages!

## Slide 46: Benefits of inter-coflow scheduling
time
2
4
6
time
2
4
6
time
2
4
6
Coflow1 comp. time = 5
Coflow2 comp. time = 6
Average FCT = 5
Coflow1 comp. time = 5
Coflow2 comp. time = 6
Average FCT = 4.33
Fair Sharing (TCP, DCTCP)
Smallest-Flow First (pFabric)
Smallest-Coflow First
Coflow1 comp. time = 3
Coflow2 comp. time = 6
Average FCT = 4.67
L1
L2
L1
L2
L1
L2
Link 1
Link 2
3 Units
Coflow 1
6 Units
Coflow 2
2 Units
Coflow completion time (CCT) is a better predictor of job-level performance than FCT
Notes: Let us see the potentials of inter-coflow scheduling through a simple example.
We have two coflows: coflow1 in black with one flow on link1 and coflow2 with two flows.
Each block represent a unit of data.
Assume, it takes a unit time time to send each unit of data.
Let’s start with considering what happens today.
In this plot, we have time in the X-axis and the links on Y-axis.
Link1 will be almost equally shared between the two flows from two different coflows and the other link will be used completely by coflow2’s flow.
After, 6 time units, both coflows will finish.
Recently, there has been a lot of focus on minimizing flow completion times by prioritizing flows of smaller size.
In that case, the orange flow in link1 will be prioritized over the black flow.
After 3 time units, the orange flow will finish.
Note that coflow2 hasn’t finished yet, because it still has 3 more data units from its flow on link2.
Eventually, when all flow finishes, the coflow completion times remain the same even thought the flow completion time has improved.
The optimal solution for minimizing application-level performance, in this case, would be to let the black coflow finish first.
As a result, we can see application-level performance improvement for coflow1 without any impact on the other coflow.
In fact, it is quite easy to show that significantly decreasing flow completion times might still not result in any improvement in user experience.

## Slide 47: How to implement coflows?
Modify applications to annotate coflows
  Possible to infer them as well [SIGCOMM’16]
Managed communication
  Applications do not communicate; instead, a central entity does the communication on their behalf
Centralized scheduling

## Slide 48: Summary
Networking in modern datacenters
  L2/L3: Source routing and load balancing to exploit multiple paths over the Clos topology
  L4: Find a better balance between latency and throughput requirements
  L7: Exploit application-level information with coflows
Last class: Review 4